## Slide 1: Create Your Own Controller!
OpenSim Developers’ Workshop | October 2009
Notes: <number>

## Slide 2: Movement control
Commands
Sensing
Body
Nervous system
http://www.cs.princeton.edu/gfx/proj/sugcon/models/brain.png
Notes: <number>

## Slide 3: Investigating movement control
Simulation
Controls/Excitations
States
Model
Controller
http://www.cs.princeton.edu/gfx/proj/sugcon/models/brain.png
Notes: <number>

## Slide 4
Controller
ControllerExample.cpp
Desired trajectory
main()
Create model
Create controller
Connect model and controller
Run simulation
Investigating movement control
Investigating movement control in OpenSim

## Slide 5
Exercise
Make a controller to do this:
Want z(t) to go from 0 to +0.15 to -0.15 to 0 in 2 seconds
1 body
2 muscles
Left (-z)
Right (+z)
Notes: <number>

## Slide 6
Controller
Desired trajectory
main()
Create model
Create controller
Connect model and controller
Run simulation
Investigating movement control in OpenSim
ControllerExample.cpp

## Slide 7: Desired trajectory
t
Want z(t) to go from 0 to +0.15 to -0.15 to 0 in 2 seconds
zdes

## Slide 8: Desired trajectory
double desiredModelZPosition( double t ) {
// z_des(t) = 0.15 sin( pi * t )
return 0.15 * sin( Pi * t );
}
ControllerExample.cpp

## Slide 9
Controller
Desired trajectory
main()
Create model
Create controller
Connect model and controller
Run simulation
Investigating movement control in OpenSim
ControllerExample.cpp

## Slide 10: Controller design
+z

## Slide 11: Controller design
+z

## Slide 12: Controller design
+z

## Slide 13: Controller design: proportional (position) control
ades = z”des + kp( zdes – z )
Fdes = m ades
if( Fdes < 0 ) { // want block to move to the left
L_muscle_excitation = |Fdes| / Fopt,L
R_muscle_excitation = 0
}
else if( Fdes > 0 ) { // want block to move to the right
L_muscle_excitation = 0
R_muscle_excitation = |Fdes| / Fopt,R
}
else { // don’t want block to move at all
L_muscle_excitation = R_muscle_excitation = 0
}
Approximation
Pretend muscles are idealized linear actuators that can only pull
muscle_force = muscle_excitation * max_isometric_force
Use position control (with position gain kp)

## Slide 14: Controller implementation: overview
class TugOfWarController : public CustomController {
public:
TugOfWarController( Model& aModel, double aKp ) :
CustomController( aModel ), kp( aKp ) {
…
}
virtual double computeControl( const SimTK::State& s, int index ) const {
…
return newControl;
}
private:
double kp;
double blockMass;
};
ControllerExample.cpp

## Slide 15: Controller implementation: computeControl
virtual double computeControl( const SimTK::State& s, int index ) const {
double t = s.getTime();
Muscle* act = dynamic_cast<Muscle*>(&_actuatorSet.get( index ));
double zdes = desiredModelZPosition(t);
double zdesa = desiredModelZAcceleration(t);
const Coordinate& zCoord = _model->getCoordinateSet().
get( “blockToGround_zTranslation” );
double z = zCoord.getValue(s);
double pErrTerm = kp * abs( zdes - z );
double desAcc = zdesa + pErrTerm;
double desFrc = desAcc * blockMass;
double Fopt = act->getMaxIsometricForce();
double newControl;
if( desFrc < 0 && index == 0 || desFrc > 0 && index == 1 )
newControl = abs( desFrc ) / Fopt;
else newControl = 0.0;
if( newControl < 0.0 ) newControl = 0.0;
if( newControl > 1.0 ) newControl = 1.0;
return newControl;
}
ControllerExample.cpp

## Slide 16: Controller implementation: constructor
TugOfWarController( Model& aModel, double aKp ) :
CustomController( aModel ), kp( aKp ) {
// Read the mass of the block.
blockMass = aModel.getBodySet().get( “block” ).getMass();
std::cout << std::endl << “blockMass = ” << blockMass
<< std::endl;
}
ControllerExample.cpp

## Slide 17
Controller
Desired trajectory
main()
Create model
Create controller
Connect model and controller
Run simulation
Investigating movement control in OpenSim
ControllerExample.cpp

## Slide 18
The main() routine
int main() {
…
// Create an OpenSim model from the model file provided.
Model osimModel( “tugOfWar_model_ThelenOnly.osim” );
…
double kp = 100.0; // position gain
…
// Controller knows about model, so
// controller can receive states and send controls
TugOfWarController *controller = new
TugOfWarController( osimModel, kp );
// Model knows about controller, so
// model can receive controls and send states
osimModel.addController( controller );
…
}
ControllerExample.cpp
Notes: <number>

## Slide 19: Run the simulation – step 1: CMake
1) Enter source directory
2) Enter build directory
3) Click Configure
5) Click Configure again
6) Click Generate
4) Enter the top-level
directory of your
OpenSim installation

## Slide 20: Run the simulation – step 2: compile program
Right-click and choose Build
Open OpenSimAPIExamples\ControllerExample\Build\ControllerExample.sln

## Slide 21: Run the simulation – step 3: run program
C:\
_
_
X
C:\Documents and Settings\ctj>cd Desktop\OpenSimAPIExamples\OpenSi
mAPIExamples\ControllerExample
C:\Documents and Settings\ctj\Desktop\OpenSimAPIExamples\OpenSimAP
IExamples\ControllerExample>Build\Release\main.exe
-------------------------------------------------------
This program includes software developed by the
Apache Software Foundation (http://www.apache.org/).
-------------------------------------------------------
Created model osimModel from file tugOfWar_model_ThelenOnly.osim
kp = 1600
kv = 80
blockMass = 20
Command Prompt

## Slide 22: Visualize the simulation
Desired motion
Proportional control
solution
kp = 100

## Slide 23: Improve your controller
Add derivative control:
  kv
  Velocity error term in control law
Increase gains:
  kp = 1600
  kv = 80
Answer is in OutputReference
Strategy: mimic kp and
position error calculation
shamelessly!
There are 10 places in
the code (labeled 1-10)
where you should make
changes.

## Slide 24: Visualize your new simulation!
Desired motion
PD control solution
kp = 1600, kv = 80