## Slide 1: Slicer Tutorial Image Editor Draw Tool
January 6, 2006
Chand T. John
Stanford University

## Slide 2: Acknowledgments
Stanford Center for Biomedical Computation
NIH U54GM072970
Thanks to Scott Delp, Allison Arnold-Rife, Thor Besier,
Silvia Salinas Blemker, Christie Draper, Kate Holzbaur
National Alliance for Medical Image Computing
Thanks to Steve Pieper, Ron Kikinis, Bill Lorensen, and all
who have contributed to the development of the 3D Slicer
and the previous editing tutorial

## Slide 3: Disclaimer
It is the responsibility of the user of 3D
Slicer to comply with both the terms of
the license and with the applicable
laws, regulations and rules.

## Slide 4: Goal of This Tutorial
Guiding you step-by-step through the
process of manual segmentation and
construction of a 3D model from a
3D medical image

## Slide 5: Slicer Editor Draw Tool

## Slide 6: Tutorial Exercise
This tutorial contains a sequence of small
exercises designed to teach you how to load
data, segment data using the image editor,
create a 3D model, and save data. Please
follow the instructions exactly as they are
given to you, and try to do the whole tutorial
in one sitting without closing Slicer in the
middle.

## Slide 7: Overview of Training
Part 1: Loading the DICOM Data
Part 2: Drawing Tools
Part 3: Model Construction
Part 4: Saving Volumes

## Slide 8: Downloading the Data
On the Slicer 101 training page:
http://wiki.na-mic.org/Wiki/index.php/Slicer:Workshops:User_Training_101
Download the Tutorial-with-dicom.zip file.
Unzip this file on your computer.

## Slide 9: Loading the DICOM Data
Click on the Data panel. When Slicer starts, the Data panel appears automatically.
Click Add Volume.

## Slide 10: Loading the DICOM Data
Click on this pull-down menubutton and choose
Dicom.
The Props tab of the Volumes panel appears.

## Slide 11: Loading the DICOM Data
Click Select DICOM Volume.
In the dialog box that pops up, choose the tutorial→dicom directory within the directory into which you unzipped the DICOM files.

## Slide 12: Loading the DICOM Data
Click Deselect All.
Click each N to turn it into an S. This selects just the first four images of this data set. You will soon segment each of these images.
Click Ok.

## Slide 13: Loading the DICOM Data
Click Header.
Click Apply.

## Slide 14: Loading the DICOM Data
The data appears in both the 3D Viewer and the three slices of the 2D Viewer.

## Slide 15: Step 1 Complete!
Part 1: Loading the DICOM Data
Part 2: Drawing Tools
Part 3: Model Construction
Part 4: Saving Volumes

## Slide 16: Manual Editor’s Anatomy
Set the labelmap value for the segments you draw. Each labelmap value (e.g. 2) has a color (e.g. Skin) associated with it.
Labelmap Settings
Point Radius
Set the thickness (in pixels) of control points you plot, and the lines connecting them. If drawing open polygons, zero is the most practical value.
Sample Density
Set the number of additional points to sample off of the spline connecting adjacent control points each time Apply is clicked. Set this to zero to use only the control points you drew as input to the ModelMaker.
Edit Menu
Pull down this menu for edit operations: Cut, Copy, Paste, Select All, Deselect All, Delete Selected, or Delete All. If you are in the Viewer window, you can use shortcut keys for most of these operations.
Leave or Clear Points
If you have many slices to segment with little change in the overall shape between slices, you can choose No so that after clicking Apply, the points you plotted will be available for editing in the next slice in which you draw.
Drawing Mode
Choose the drawing mode. Draw allows you to plot new points at the end of the current polygon, while Insert allows you to add points between existing points. Select and Move are one mode, which Slicer toggles between automatically based on mouse pointer location.
Apply
Click this when you are done drawing a polygon, and it will be saved as part of the labelmap volume that will be the input into the ModelMaker.
Unapply
Click this button to scroll through all polygons that have been applied on a slice and re-edit any of them. It is a general version of an undo feature just for the Apply operation.
Peek Under Labelmap
This button toggles between whether the applied polygons are visible or not in the Viewer window. This can help if you feel like the existing labelmap is obscuring your view of the underlying image.
Contour Topology and Shape
Choose whether you want the polygon you draw to be closed or open (the former is when the last point and first point of the contour are adjoined, the latter is when they are not), and whether it should be a filled region or just a set of points.
Rendering Mode
Choose whether you want the Viewer window to update only the 2D window you are working in, or all three 2D windows, or in all 2D windows and the 3D window.
Leave or Clear Labelmap
If you choose Yes for this option, the labelmap will be cleared each time you click Apply. Choose No if you want to keep the labelmap created from other Editor tools such as the Threshold tool.
Spline Mode
If you choose Yes for this option, the a cardinal spline will be interpolated through the control points of the polygon you are currently editing. If you choose No, only the original control points will be used in any operation involving this polygon.

## Slide 17: Segmentation
Segmentation: separating and labeling anatomical structure images.
Result is a label map.
Semi-automatic process using editing tools.
  Include thresholding, morphological operations, island-removal, and free-hand drawing.
  Segment data in 3D or slice-by-slice.
Merge volumes to construct complex images.
Example: segment skin from an MR scan.
Notes: Segmentation Guide
You can segment volumetric data semi-automatically using editing tools such as thresholding, morphological operations, island-removal, free-hand drawing, and more.
top
3a. Introduction
You can apply editing effects to the data on a 3D or slice-by-slice basis.
For instance, you can perform slice-by-slice editing on either the axial, coronal, or sagittal slices simply by clicking on the appropriate slice.
In addition, you may apply each effect to either the original volume, or a working volume.
Furthermore, you may apply multiple editing effects to the working volume, and, when finished, merge the working volume with a composite volume to overlay smaller structures onto larger ones.
For example, we can segment skin automatically from an MR scan, by applying a threshold at the first trough of the histogram (where the noise and signal lobes overlap) and then storing the binary output in the working volume. We next remove islands in the working volume, and finish with an erosion and dilation to smooth the edges. At this point, we copy this working volume to the composite volume. Next, we can segment the brain in the working volume. All non-zero voxels of the working volume can overwrite the composite volume to form a combination of skin and brain.
One strength of our system is that you can visualize effects by overlaying the working volume translucently on the original volume and exploring the result in the 3D view.

## Slide 18: Drawing a Polygon
Click Editor. Change name of labelmap if you wish. Default is Working. Click Start Editing.
Note Active Slice is Red.
Click Draw2.
In View menu, choose 1 x 512.
In Viewer window, click on AxiSlice and choose SagSlice in the menu that pops up.
In that 2D Viewer window, plot points in the order shown in the image on the left.
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Polyline
Catmull-Rom Spline

## Slide 19: Inserting Points
In the Menu window, currently the Draw mode is selected. Click Insert to change to Insert mode.
Click on the 2D Viewer to insert points in the order shown in the image to the left.
Then click Apply in the Menu window. This adds a filled polygon to the labelmap.
Click Unapply, then Points, then Apply. Note now the labelmap contains only pixels representing individual points, instead of an entire region.
1
2
3
4
5
6
7

## Slide 20: Setting Polygon Type
Now try clicking Unapply, then Open, then Apply. Note that now the labelmap contains an open set of points instead of a closed one.
Click Unapply, then Polygon, then Apply. Now the labelmap contains an open polyline with the thickness specified by the number in the Point Radius field.

## Slide 21: Changing Point Radius
Click Unapply.
In the Point Radius field, change 2 to 0 and press Enter.
Click Open and Polygon if they are not already selected.
Click Apply.
Note the thickness of the applied polyline is now only one pixel.

## Slide 22: Setting Sample Density
Click Unapply.
In the Sample Density field, change 2 to 10 and press Enter.
Click Closed and Polygon if they are not already selected.
Click Apply.
Note the polygon’s boundary is now smoother due to the denser sampling of each curve segment.

## Slide 23: Selecting, Moving Points
Click Unapply.
Click Select in the Menu window.
On the 2D Viewer window, click and drag the mouse over some control points. The selected points are yellow, while the others are the color of the labelmap you chose.
Move the mouse onto one of the selected points, or onto one of the lines connecting those points. The mode automatically changes to Move. If you move the mouse away, the mode changes back to Select.
Now move the mouse pointer to one of the selected points, press and hold the left mouse button, and then move the mouse around. Note the selected points move as your mouse pointer moves.
Release the left mouse button. Practice modifying the polygon more if you wish. When finished, click Apply.

## Slide 24: Selecting Multiple Times
To select multiple groups of points, select the first group of points as in the previous slide.
Then select each subsequent group of points by holding the Control key on the keyboard as you click and drag the mouse.

## Slide 25: Deselecting All Points
Click Unapply.
Click Select in the Menu window.
Click on the 2D Viewer window away from the control polygon. Note all points become deselected.
You can also deselect all points by choosing Deselect All in the Edit: menu in the Menu window.

## Slide 26: Selecting All Points
Make sure the draw mode is still Select.
Click in the 2D Viewer window, away from the polygon. This is just to make the Viewer window active.
Press and hold the Control key on the keyboard, and then press A. Note this selects all control points.
This operation can also be done by choosing Select All from the Edit: menu in the Menu window.

## Slide 27: Deleting Selected Points
Now click away from the polygon in the 2D Viewer window. This deselects all points.
Click and drag the mouse to select one or two points of the polygon.
Press the Delete key on the keyboard. This deletes the point(s) you selected.
The same operation can be done by choosing Delete Selected from the Edit: menu in the Menu window.

## Slide 28: Cutting, Copying, Pasting
Make sure the draw mode is still Select.
Click in the 2D Viewer window, away from the polygon. This is just to make the Viewer window active.
Press Control, X. This copies the whole polygon to Slicer’s polygon clipboard, and deletes the polygon from the Viewer.
Press Control, V. This pastes the whole polygon back onto the Viewer.
Pressing Control, C will copy the polygon to the clipboard without deleting the points from the Viewer.
These operations are also available in the Edit: menu as Cut, Paste, and Copy, respectively.

## Slide 29: Deleting All Points
Make sure the draw mode is still Select.
Click in the 2D Viewer window, away from the polygon. This is just to make the Viewer window active.
Press Control, D. This deletes the entire polygon from the Viewer, and does not store it on the clipboard.
This operation is also available as Delete All in the Edit: menu in the Menu window.
Fortunately, the polygon is still in the clipboard from our exercise on the previous slide. Press Control, V to paste it back onto the Viewer.

## Slide 30: Delete Points After Apply
Now in the Menu window, next to the label Delete points after apply:, click No.
Now click Apply.
Note that, unlike when Yes was selected for Delete points after apply:, the control polygon is now deleted after you click Apply. This option is useful when you have many slices in which to segment a structure that changes shape very little between slices.

## Slide 31: Deletion
To delete a whole polygon, simply go to the slice containing the polygon and click Unapply repeatedly until the polygon you want is selected.
Then press Control+D, or choose Delete All from the Edit: menu.
Click Apply.
To delete part of a labelmap region, simply choose the Output: to be black, and then draw and apply a polygon in the area you wish to clear. However, this will delete only the labelmap, not the polygon; in fact it will add this extra polygon to the stack, so this method of deleting a contour is no longer recommended.

## Slide 32: Arrow Key Shortcuts
Click Unapply. The polygon you just applied reappears.
Make sure the draw mode is Select, and click in the Viewer window to make the window active.
Press the Down Arrow on your keyboard three times. This changes the draw mode from Select/Move to Insert to Draw and back to Select.
Press the Up Arrow on your keyboard. This is a shortcut key for the Apply operation.
Press the Right Arrow key. This moves you to the next slice in the 2D Viewer window. Press the Left Arrow to go back to the original slice.

## Slide 33: Shortcut Key Reference
Control+X Cut
Control+C Copy
Control+V Paste
Control+A Select All
Delete Delete Selected
Control+D Delete All
Up Apply
Down Change Draw Mode
Right Forward one slice
Left Back one slice

## Slide 34: Step 2 Complete!
Part 1: Loading the DICOM Data
Part 2: Drawing Tools
Part 3: Model Construction
Part 4: Saving Volumes

## Slide 35: Finish Segmenting
Currently Slicer requires you to segment every slice of image data before you create a 3D model.
Use the tools from the previous exercise to draw and apply a polygon in each of the remaining three slices. Don’t worry about accuracy for now, a rough segmentation will suffice.

## Slide 36: Go to the ModelMaker
Click on the Effects tab.
Click Make Model.

## Slide 37: Create the Model
You may rename your model if you wish.
Click Create.
This takes you to the Create tab of the ModelMaker.

## Slide 38: Create the Model
Slicer has performed marching cubes, decimation, and smoothing to create the model.

## Slide 39: Viewing the Model
In the View menu, click Normal.
Deselect each V in the 2D Viewer.
This removes the three viewing planes from the 3D Viewer, allowing you to see the model you created.

## Slide 40: Backface Culling
Backface culling is a way to speed up rendering of 3D shapes by simply not rendering any part of a shape that the viewer can’t see.
Backface culling is useful for rendering closed 3D meshes, but we must turn it off for open meshes, like the one we just created.

## Slide 41: Turn off Backface Culling
Click Models in the Main menu.
The Display tab appears.
Right-click on the name of your model in the Visibility list.
A menu pops up.
Uncheck Backface Culling.
Now your model is rendered properly in the 3D Viewer.

## Slide 42: Step 3 Complete!
Part 1: Loading the DICOM Data
Part 2: Drawing Tools
Part 3: Model Construction
Part 4: Saving Volumes

## Slide 43: Saving Segmented Data
Segmented data: a label map
On the Main menu, click Editor.
  The Editor panel appears.
Click the Volumes tab.
The Volumes tab appears.
Select Save.
Select the name of your label map for Volume to Save.
Select a file name.
  Simplest to use same name as the Volume to Save.
Select Standard or .pts for format.
Save file to the appropriate directory.
Usual Slicer save format is Standard.
.pts saves a labelmap as a .pts file in which each line is of the form “x y z” where (x,y,z) are the RAS coordinates (in millimeters) of a voxel in the labelmap.
Notes: Save your segmented data (called a "label map").
On the Main menu, click Editor. The Editor panel appears.
Click the Volumes tab. The Volumes tab appears.
Select Save.
Select the name of your label map for Volume to Save.
Select a file name. It is often simplest to use the same name as the Volume to Save.
Save this file to the appropriate directory.

## Slide 44: Exercise: Saving Volume
Click Editor  Volumes tab  Save
Select the Volume to Save. This can be the labelmap or the model you created.
Note that if you save a model, you must choose Standard under Pick Format. If you are saving a labelmap, you may choose either Standard or .pts.
Add file name to end of Filename Path.
Click Save.
Repeat this exercise with a model if you saved a labelmap, and with a labelmap if you saved a model. Note what files are written out as a result.

## Slide 45: Conclusion
You may now exit Slicer! 
Drawing tools more similar to standard drawing programs and image processing software
Open-source environment