## Slide 1: Controller for Maintaining Balance
ME 281: The Biomechanics of Movement
BIOE/ME 485: Modeling and
Simulation of Human Movement
Mishel Johns and Chris Ploch
Notes: <number>

## Slide 2
BIOE/ME 485: Modeling and Simulation of Human Movement
Goal: to design a controller that uses IAA to maintain balance
  Work with Gait2392 model
  Also general enough to work with other models
Is accelerating the COM to the desired location sufficient to maintain balance?
STRATEGY
RESULTS
CONCLUSIONS
CONTRIBUTIONS
CHALLENGE
Notes: <number>

## Slide 3
BIOE/ME 485: Modeling and Simulation of Human Movement
Develop IAA solver
  Interface IAA with controller
Create IAA controller
  Determine muscle forces for desired COM acceleration
Test with multiple models:
  3DOF block
  Standing model with fewer muscles
  Standing model with more muscles
CHALLENGE
STRATEGY
RESULTS
CONCLUSIONS
CONTRIBUTIONS
Notes: <number>

## Slide 4
BIOE/ME 485: Modeling and Simulation of Human Movement
Controller layout:
Class IAAController
  New IAAController(Kp, Kv, &osimModel)
  Creates a copy of the model, with the controllers and visualizer removed
  This copy is used for IAA and calculating CoM accelerations
Integrator: RungeKuttaMerson
  Works better with fixed time steps (accuracy untested)
CHALLENGE
STRATEGY
RESULTS
CONCLUSIONS
CONTRIBUTIONS
Notes: <number>

## Slide 5
BIOE/ME 485: Modeling and Simulation of Human Movement
Class IAAController:
  Determines desired acceleration
  Solves Ax = B to find x
    A = matrix of induced accelerations
    B = desired accelerations
    x = forces to produce desired accelerations
  Weighted by 1/Fmax and muscle limits are enforced
  General norm minimization with equality constraints - Min ||Wx||; subject to Ax = B
CHALLENGE
STRATEGY
RESULTS
CONCLUSIONS
CONTRIBUTIONS
Notes: <number>

## Slide 6
BIOE/ME 485: Modeling and Simulation of Human Movement
Apply controller to 3DOF block and more complicated standing models.
CHALLENGE
STRATEGY
RESULTS
CONCLUSIONS
CONTRIBUTIONS
Notes: <number>

## Slide 7
BIOE/ME 485: Modeling and Simulation of Human Movement
Succeeded in controlling 3DOF block
Attempts to keep standing model upright but struggles
Simulation speed too slow
Not properly treating muscle dynamics
CHALLENGE
STRATEGY
RESULTS
CONCLUSIONS
CONTRIBUTIONS
Notes: <number>

## Slide 8
BIOE/ME 485: Modeling and Simulation of Human Movement
IAA controller works but the standing models have problems
Ideas for fixing problems:
  Control angle of torso
  Control all generalized coordinates
Other future steps:
  Properly treat muscle dynamics
  Fix nonstandard usage of OpenSim functions
  Use foot contact model instead of welding
CHALLENGE
STRATEGY
RESULTS
CONCLUSIONS
CONTRIBUTIONS
Notes: <number>

## Slide 9
BIOE/ME 485: Modeling and Simulation of Human Movement
Convenient controller compatible with many models
Uses:
  Test resistance to perturbation
  Compare different balance types
  Compare results to activation patterns in literature
CHALLENGE
STRATEGY
RESULTS
CONCLUSIONS
CONTRIBUTIONS
Notes: <number>

## Slide 10
BIOE/ME 485: Modeling and Simulation of Human Movement
Acknowledgements:
Ajay Seth
Tom Uchida
Matt DeMers
Daniel Jacobs
CHALLENGE
STRATEGY
RESULTS
CONCLUSIONS
CONTRIBUTIONS
Notes: <number>