## Slide 1: BME 498: Simulation of Human Movement
Residual Reduction Algorithm

## Slide 2: OpenSim Analyses
Scaling
Inverse Kinematics
Inverse Dynamics
Residual Reduction Analysis
Computed Muscle Control

## Slide 3: What are residuals?
Non-physical forces and torques that account for inconsistencies between experimental GRFs and joint accelerations estimated from experimental markers.
Inconsistencies due to:
  noise in marker and joint angle data
  inaccuracies in model geometry and mass distribution

## Slide 4: Why do residuals need to be reduced?
Residuals are non-physical and necessary only to account for errors
Want muscles to account for all movement to have confidence in muscle contributions

## Slide 5: How can residuals be reduced?
Adjust mass distribution, including Torso COM location
Adjust kinematics slightly while satisfying equations of motion
Add forces and moments to the pelvis

## Slide 6: Residual Reduction Algorithm (RRA)
Recommends mass adjustments and forces to pelvis to make F = ma
http://simtk-confluence.stanford.edu:8080/display/OpenSim/Simulation+with+OpenSim+-+Best+Practices

## Slide 7: RRA Sample Calculation: Reduce Forward-Backward Rocking
T + MZ = I*α
Make this residual as small as possible

## Slide 8: RRA Sample Calculation: Reduce Forward-Backward Rocking
Alter just torso center of mass
Reduce residual R by amount dR
mg
r0
mg
r1

## Slide 9: RRA Sample Calculation: Reduce Forward-Backward Rocking
Alter torso flexion-extension
mg
r1
Length r1 = length of r0
mg
r0

## Slide 10: RRA in OpenSim
Many options to reduce residuals:
  Adjust mass distribution, including Torso COM location
  Adjust kinematics slightly while satisfying equations of motion
  Add forces and moments to the pelvis
How are all of these simultaneously altered to reduce residuals?
  Uses a feedback controller and cost function, similar to CMC…more on this later