## Slide 1: BME 498: Simulation of Human Movement
Introduction to Motion Capture, Anatomy, and OpenSim

## Slide 2: Modeling and Simulation Process
Different analyses available
Musculoskeletal Model Components

## Slide 3: Overview: Human Simulation of Movement
Collect motion capture data
Analyze the data:
  Scale
  Inverse Kinematics
  Inverse Dynamics
  Reduced Residual Analysis
  Computed Muscle Control
Notes: http://www-personal.umich.edu/~hamms/portfolio/motioncapture/index.html

## Slide 4: Motion Capture Data: Application
Notes: http://wps92.wordpress.com/motion-capture/

## Slide 5: Motion Capture Data: Application
Notes: http://www.funnyjunk.com/Orc+face+motion+capture/funny-gifs/4932186/

## Slide 6: Motion Capture Data
Infrared cameras
Retroreflective markers
Force plate
3d coordinates of markers
Force of the ground on the person’s feet
Notes: http://en.wikipedia.org/wiki/Motion_capture#mediaviewer/File:MotionCapture.jpg

## Slide 7: OpenSim
3d coordinates of markers
Force of the ground on the person’s feet
Joint angles (for animations)
Joint forces
Muscle forces

## Slide 8: OpenSim Analyses
Scaling
Inputs: experimental markers, generic model
Output: subject-specific model

## Slide 9: OpenSim Analyses
Scaling
Inverse Kinematics
Inputs: experimental markers, scaled model
Output: joint angles

## Slide 10: OpenSim Analyses
Scaling
Inverse Kinematics
Inverse Dynamics
Inputs: joint angles, force data
Output: joint torques and forces

## Slide 11: OpenSim Analyses
Scaling
Inverse Kinematics
Inverse Dynamics
Residual Reduction Analysis
Inputs: joint angles, joint torques, joint forces, force data
Output: residuals

## Slide 12: OpenSim Analyses
Scaling
Inverse Kinematics
Inverse Dynamics
Residual Reduction Analysis
Computed Muscle Control
Inputs: joint angles, joint torques, joint forces, residuals, force data
Outputs: muscle forces

## Slide 13: Musculoskeletal Model Components
Skeleton
Joints
Muscles

## Slide 14: Skeleton
Bony geometry digitized from 23 cadavers by Delp et al
Generic geometry is for a 73 kg male

## Slide 15: Joints
Each joint has a number of degrees of freedom (dof)
  Each degree of freedom = generalized coordinate
Joints can be represented using various models:
  Hinge (1 dof)
  Ball-and-socket (3 dof)
  Fully 6 dof joint

## Slide 16: Muscles: Properties
Hill muscle model
Force-length properties
Force also depends on excitation (input from nervous system)
Force depends on how fast joint is moving
More on this later…
Notes: http://simtk-confluence.stanford.edu:8080/display/OpenSim/Thelen+2003+Muscle+Model

## Slide 17: Muscles: Geometry
Muscles attach to relevant bony landmarks
Represented as line segments with tendon-muscle fibers-tendon in series
Based on cadavers and knowledge of anatomy
See Henry Gray’s Human Anatomy for more details on each muscle

## Slide 18: Muscles: Geometry
Muscles can have very broad attachments to the bones
Represent as many line segments

## Slide 19: Muscles: Uniarticular versus Biarticular
Uniarticular: Cross 1 joint
Biarticular: Cross 2 joints
Notes: http://3.bp.blogspot.com/-DgbdCj5r_Rw/TW1sXWtOSqI/AAAAAAAAAac/stHY3HLPelI/s320/Hip-Rotators.jpg
http://www.criticalbench.com/muscles/hamstrings-anatomy.jpg

## Slide 20: Muscles: Uniarticular versus Biarticular
GA
SOL

## Slide 21: Muscle Moment Arms
Notes: StradivariusTV, 2009, Wikipedia

## Slide 23
Gastroc medialis
Gastroc lateralis
Plantaris

## Slide 24: How to Calculate Moment Arm: Tendon Excursion Method
Measure: muscle length as a function of angle
Calculate: differentiate

## Slide 26: How to Calculate Moment Arm: Tendon Excursion Method
Work done in stretching/shortening of muscle
Bone motion (kinetic energy)
+
F * dx
Stretching of tendon (potential energy)
Work = Force*distance
Work = Torque*angle
=
Work to stretch ligament
ignored
+
Work to displace bones
Work to rotate bones
+
ignored

## Slide 27
F * dx
=
Work to rotate bones
M1*dΘflex/extend +
M2*dΘabb/abd +
M3*dΘint/ext
F * dx
=
ignored
ignored
F* dx = M1*dΘflex/extend
Torque = moment arm*force
Moment Arm = dx/ dΘflex/extend
This makes in more of a 2D method.

## Slide 28: 3D Extension – OpenSim
F * dx
=
Work to stretch ligament
+
Work to displace bones
Work to rotate bones
+
ignored
No longer ignored
Consider rotations in 3 directions

## Slide 29
From the chain rule…
F * dx
=
Work to displace bones
Work to rotate bones
+
M1*dΘ1 + M2*dΘ2 + M3*dΘ3
F1*dl1 + F2*dl2 + F3*dl3
Remember: Moment arm = torque/force

## Slide 30
Moment arms to cause 3 rotations
Moment arms to cause 3 translations

## Slide 31: Anatomy
Medial-lateral
Proximal-distal
Notes: http://montagepages.fuselabs.com/public/kayla/AnatomicalDirectionsandPositions/7607b18e-0fd6-4920-b81a-899d859e448d.htm

## Slide 32: Anatomy
Notes: http://www.gla.ac.uk/t4/~fbls/files/fab/tutorial/anatomy/hip1.html

## Slide 33: Gait Cycle
Heel contact
Toe-off
Stance: phase in which the limb is in contact with the ground
Initial contact—Instant the foot contacts the ground
Swing: phase in which the foot is in the air for limb advancement
Loading response—Time period from immediately following initial contact to the lift of the contralateral extremity from the ground, during which weight shift occurs
Midstance—Time interval from lift of the contralateral extremity from the ground to the point where the ankles of both extremities are aligned in the frontal (or coronal) plane
Terminal stance—Period from ankle alignment in the frontal plane to just prior to initial contact of the contralateral (swinging) extremity
Initial swing—Lift of the extremity from the ground to position of maximum knee flexion
Mid swing—Immediately following knee flexion to vertical tibia position
Terminal swing—Following vertical tibia position to just prior to initial contact
Notes: http://www.foundationpilates.com/happens-walk-gait-cycle-overview/

## Slide 34: Modeling and Simulation Process
Musculoskeletal Model Components
Lab 2