Meshlab

1. ACL (combined model of axial, first sagittal, and redone sagittal planes) – ACL COARSE
- Surface Reconstruction: VCG
  - World Unit: .7
  - Post Merge Simplification Box checked
- Laplacian Smooth (for all)
  - Unchecked 1D Boundary Smoothing Box
  - Smoothing Steps: 5
- Quadratic edge collapse decimation
  - .35%
- Iso Parametrization
  - Used Default
- Iso Parametrization Remeshing
  - Used value of 2
- Laplacian Smooth (big bumps)
  - Smoothing Steps: 1
- Hausdorff Distance
  - min: 0.000202 max: 1.205479	mean: 0.309804	RMS: 0.394811
- Colorize by Vertex Quality
  - min: 0.000725	max: 0.923
- For Smoothing after trimmed with femur and tibia:
  - Laplacian Smooth
    - Unchecked 1D Boundary Smoothing Box
    - Smoothing Steps: 1
  - Surface Reconstructin VCG
    - World Unit: .2
    - Post Merge Simplification Box checked
  - Iso Parameterization
    - used default
  - Iso Parameterization Remeshing
    - Used value of 2

2. ACL (combined model of axial, first sagittal, and redone sagittal planes) – ACL MODERATE
- Surface Reconstruction: VCG
  - World Unit: .7
  - Post Merge Simplification Box checked
- Laplacian Smooth (for all)
  - Unchecked 1D Boundary Smoothing Box
  - Smoothing Steps: 5
- Quadratic edge collapse decimation
  - .5%
- Iso Parametrization
  - Used Default
- Iso Parametrization Remeshing
  - Used value of 3
- Laplacian Smooth (big bumps)
  - Unchecked 1D Boundary Smoothing Box
  - Smoothing Steps: 3
- Hausdorff Distance
  - min: 0.000034 max: 1.193308	mean: 0.264572	RMS: 0.336324
- Colorize by Vertex Quality
  - min: 0.000484	max: 1.19
- For Smoothing after trimmed with femur and tibia:
  - Laplacian Smooth
    - Unchecked 1D Boundary Smoothing Box
    - Smoothing Steps: 1
  - Surface Reconstructin VCG
    - World Unit: .2
    - Post Merge Simplification Box checked
  - Iso Parameterization
    - used default
  - Iso Parameterization Remeshing
    - Used value of 3

3. ACL (combined model of axial, first sagittal, and redone sagittal planes) – ACL FINE
- Surface Reconstruction: VCG
  - World Unit: .7
  - Post Merge Simplification Box checked
- Laplacian Smooth (for all)
  - Unchecked 1D Boundary Smoothing Box
  - Smoothing Steps: 5
- Quadratic edge collapse decimation
  - .5%
- Iso Parametrization
  - Used Default
- Iso Parametrization Remeshing
  - Used value of 4
- Laplacian Smooth (big bumps)
  - Unchecked 1D Boundary Smoothing Box
  - Smoothing Steps: 3
- Hausdorff Distance
  - min: 0.000107 max: 1.098842	mean: 0.254618	RMS: 0.322604
- Colorize by Vertex Quality
  - min: 0.00023	max: 1.08
- For Smoothing after trimmed with femur and tibia:
  - Laplacian Smooth
    - Unchecked 1D Boundary Smoothing Box
    - Smoothing Steps: 1
  - Surface Reconstructin VCG
    - World Unit: .2
    - Post Merge Simplification Box checked
  - Iso Parameterization
    - used default
  - Iso Parameterization Remeshing
    - Used value of 4