Meshlab

1. Femur – FEMUR COARSE
- Surface Reconstruction: VCG
  - World Unit: 1
  - Post Merge Simplification Box checked
- Quadratic Edge Decimation
  - percent reduction= .35
- Iso Parametrization
  - Used Default
- Iso Parametrization Remeshing
  - Used value of 5
- Laplacian Smooth (for stem portion of femur)
  - Smoothing Steps: 5
  - Unchecked 1D Boundary Smoothing Box
- Hausdorff Distance
  - min: 0.000004	max: 2.414879	mean: 0.519516	RMS: 0.667782
- Colorize by Vertex Quality
  - min: 0.0000362	max: 2.41

2. Femur – FEMUR MODERATE
- Surface Reconstruction: VCG
  - World Unit: 1
  - Post Merge Simplification Box checked
- Quadratic Edge Decimation
  - percent reduction= .35
- Iso Parametrization
  - Used Default
- Iso Parametrization Remeshing
  - Used value of 8
- Laplacian Smooth (for stem portion of femur)
  - Smoothing Steps: 5
  - Unchecked 1D Boundary Smoothing Box
- Hausdorff Distance
  - min: 0.000000	max: 1.499940	mean: 0.245536	RMS: 0.322836
- Colorize by Vertex Quality
  - min: 0.00000477	max: 1.4

3. Femur – FEMUR FINE
- Surface Reconstruction: VCG
  - World Unit: 1
  - Post Merge Simplification Box checked
- Iso Parametrization
  - Used Default
- Iso Parametrization Remeshing
  - Used value of 17
- Laplacian Smooth (for stem portion of femur)
  - Smoothing Steps: 10
  - Unchecked 1D Boundary Smoothing Box
- Hausdorff Distance
  - min: 0.000000	max: 1.250311	mean: 0.148866	RMS: 0.200973
- Colorize by Vertex Quality
  - min: 0.000000	max: .8 (max originally: 1.1)