Meshlab

1. PCL (combined model composed of saggital and coronal planes) – COARSE
- Surface Reconstruction: VCG
  - World Unit: .6
  - Post Merge Simplification Box checked
- Quadratic Edge Decimation
  - percent reduction= .5
- Laplacian Smooth (for all)
  - Smoothing Steps: 5
  - Unchecked 1D Boundary Smoothing Box
- Iso Parametrization
  - Used Default
- Iso Parametrization Remeshing
  - Used value of 2
- Laplacian Smooth (for areas with bad mesh and large protrusions)
  - Smoothing Steps: 1
  - Unchecked 1D Boundary Smoothing Box
- Hausdorff Distance
  - min: 0.001495	max: 1.388722	mean: 0.308661	RMS: 0.388778
- Colorize by Vertex Quality
  - min: 0.0016	max: 1.15
- For Smoothing after trimmed with femur and tibia:
  - Surface Reconstructin VCG
    - World Unit: .3
    - Post Merge Simplification Box checked
  - Iso Parametrization
    - Used Default
  - Iso Parametrization Remeshing
    - Used value of 2

2. PCL (combined model composed of saggital and coronal planes) – MODERATE
- Surface Reconstruction: VCG
  - World Unit: .6
  - Post Merge Simplification Box checked
- Quadratic Edge Decimation
  - percent reduction= .5
- Laplacian Smooth (for all)
  - Smoothing Steps: 5
  - Unchecked 1D Boundary Smoothing Box
- Iso Parametrization
  - Used Default
- Iso Parametrization Remeshing
  - Used value of 3
- Laplacian Smooth (for areas with bad mesh and large protrusions)
  - Smoothing Steps: 5 (15 for one really large protrusion)
  - Unchecked 1D Boundary Smoothing Box
- Hausdorff Distance
  - min: 0.000122	max: 1.536209	mean: 0.286073	RMS: 0.360431
- Colorize by Vertex Quality
  - min: 0.000153	max: 1.45
- For Smoothing after trimmed with femur and tibia:
  - Surface Reconstructin VCG
    - World Unit: .3
    - Post Merge Simplification Box checked
  - Quadratic edge collpase decimation
    - .5%
  - Iso Parametrization
    - Used Default
  - Iso Parametrization Remeshing
    Used value of 3

3. PCL (combined model composed of saggital and coronal planes) - FINE
- Surface Reconstruction: VCG
  - World Unit: .6
  - Post Merge Simplification Box checked
- Quadratic Edge Decimation
  - percent reduction= .35
- Laplacian Smooth (for all)
  - Smoothing Steps: 5
  - Unchecked 1D Boundary Smoothing Box
- Iso Parametrization
  - Used Default
- Iso Parametrization Remeshing
  - Used value of 5
- Laplacian Smooth (for areas with bad mesh and large protrusions)
  - Smoothing Steps: 3 (15 for one really large protrusion)
  - Unchecked 1D Boundary Smoothing Box
- Hausdorff Distance
  - min: 0.000000	max: 0.033958	mean: 0.005049	RMS: 0.006657
- Colorize by Vertex Quality
  - min: 0.0000381	max: 1.3 (was originally set at 1.52)
- For Smoothing after trimmed with femur and tibia:
  - Surface Reconstructin VCG
    - World Unit: .3
    - Post Merge Simplification Box checked
  - Quadratic edge collpase decimation
    - .5%
  - Iso Parametrization
    - Used Default
  - Iso Parametrization Remeshing
    - Used value of 2