Meshlab

1. Tibia – COARSE
- Surface Reconstruction: VCG
  - World Unit: .9
  - Post Merge Simplification Box checked
- Iso Parametrization
  - Used Default
- Iso Parametrization Remeshing
  - Used value of 4
- Laplacian Smooth (excluding near attachment sites)
  - Smoothing Steps: 5
  - Unchecked 1D Boundary Smoothing Box
- Hausdorff Distance
  - min: 0.000015	max: 2.666996	mean: 0.493537	RMS: 0.663765
- Colorize by Vertex Quality
  - min: 0.00021	max: 2.67

2. Tibia – MODERATE
- Surface Reconstruction: VCG
  - World Unit: 1
  - Post Merge Simplification Box checked
- Quadratic Edge Collpase Decimation
  - .45
- Iso Parametrization
  - Used Default
- Iso Parametrization Remeshing
  - Used value of 6
- Laplacian Smooth (excluding near attachment sites)
  - Smoothing Steps: 5
  - Unchecked 1D Boundary Smoothing Box
- Hausdorff Distance
  - min: 0.000000	max: 1.859219	mean: 0.275036	RMS: 0.391197
- Colorize by Vertex Quality
  - min: 0.0000114	max: 1.86

3. Tibia – FINE
- Surface Reconstruction: VCG
  - World Unit: .9
  - Post Merge Simplification Box checked
- Iso Parametrization
  - Used Default
- Iso Parametrization Remeshing
  - Used value of 10
- Laplacian Smooth (excluding near attachment sites)
  - Smoothing Steps: 5
  - Unchecked 1D Boundary Smoothing Box
- Hausdorff Distance
  - min: 0.000000	max: 1.355654	mean: 0.151472	RMS: 0.215992
- Colorize by Vertex Quality
  - min: 0.000000	max: 1.21