The nature of the elastic component of articular cartilage in close proximity to the resident cells (chondrocytes), the pericellular matrix (PCM) and territorial matrix (TM), has been further illuminated by recent work using atomic force microscopy. By probing the PCM and TM at grid points around the chondrocytes, a spatial map of the elastic moduli has been obtained for both healthy and osteoarthritic (OA) tissues. Using these data, finite element (FE) models of a healthy and an osteoarthritic chondrocyte were constructed, which incorporate the change in modulus that was observed when progressing radially from the chondrocyte membrane (Figure 1C).

To apply physiological-like boundary conditions to these cellular scale models, a multiscale approach was used. A simplified model of the medial knee compartment with representation of the trilaminar cartilage, meniscus, and bones was created (Figure 1A). All structures were assigned non-linear biphasic material properties. Anistropy in both the solid and fluid phases was modelled for the cartilage and meniscus via ellipsoidal fibre distribution functions appropriate for the tissue or tissue regions. Biphasic contact constraints were enforced between articulating surfaces. A 10% nominal compression of the joint space applied over 0.5s and held for an additional 299.5s was simulated. This was done for both normal and OA cartilage material properties.

The displacements and fluid pressures calculated by these knee-scale models were then interpolated to serve as boundary conditions in the normal and OA cellular scale models, as if they were positioned in the middle zone of the femoral cartilage (Figure 1B). The cellular mechanics were then compared between normal and OA conditions, with the OA cell surprisingly experiencing less deformation (Figure 1D). To assess whether the modelling the spatial variation of the PCM and TM properties offered any advantage to simply assigning one lumped property to the regions, volumetrically averaged properties were assigned to two 3 micron thick regions (Figure 1C), for both normal and OA cases. The results of these models were then compared to the transitional cases (Figure 1D). Modelling the transition of the PCM/TM material properties proved important for normal cartilage, but negligible for the OA case.