Summary of du02 Mesh Properties Confirmation

Aiming to get within 2 standard deviations of the literature stiffness values for each tissue
Ligaments:
Tissue	Displacement in fiber direction [mm]	Desired Linear Stiffness Range [N/mm]	Initial guess c5	Measured linear stiffness [N/mm]	Final guess c5	Measured Linear stiffness / [N/mm]
ACL_IP6	3	242±28	535	122	5000	225
LCL_IP6	5	59±12	467	18	4000	47
MCL_IP7	5	63±14	467	93	300	74
PCL_IP4	3	258±62	431	283	431	283

Tendons:
Tissue	Displacement in fiber direction [mm]	Desired Modulus Range [MPa]	Reference length [mm], cross sectional area [mm^2]	Initial guess c5	Measured linear stiffness K [N/mm], / Modulus E [MPa]	Final guess c5	Measured linear stiffness K [N/mm], / Modulus E [MPa]
PTL_IP6	5	337.8.±67.7	L=48.6245 / A=35.8423	777.56	K=441.1216 / E = 598.435	337.8	K=277.62 / E=376.626
QAT_IP4	5	255.3±64.1	L=54.4644 / A=68.3829	777.56	K =865.105 / E =689.023	255.3	K= 447.696 / E= 356.57

* when c5 was set to the average modulus in the range, measured modulus fell within 2 standard deviations, which is a good sanity check.

Cartilage:
Tissue	Desired Linear Stiffness Range [N/mm]	Initial guess c1, K	Measured linear stiffness [N/mm]	Final guess c1, K	Measured linear stiffness [N/mm]
TBC-L_IP6	20.38±5.32	C1 = 2.54 / K=100	53.25	C1 = 1.1 / K=44	23.65

These properties will be applied to all cartilage tissues in the knee.

Higher mesh density cartilage was tested too (see oks003 notes) TBC-L_IP12 stiffness was measured as 30.4 N/mm

Meniscus:
c5 will be set to 92 Mpa as it fall within the range of reported values.