Open Knees oks003

Individual Tissue Testing:
as per Ahmet and Ariel's meeting on 09/18/18 several 'reduced' models were created to test tissues one at a time.

ModelReduction.py script was written to assist in automating the process of creating the test cases. The script does the following:
- as input take the febio file of the full knee model, and then names of the tissues to include.
-MPFL, LPFL springs are removed
-all tissue materials which are not to be included in the model are changed to rigid bodies
-the rigid bodies are fixed in place (with the exception of the imaginary links in the cylindrical joints describing the tibofemoral and patellofemoral joints)
-all irrelevant ties/contacts are removed
=====Note: It would be better if we completely removed any unwanted tissues, and re-numbered the materials, but trying this is causing an error with surface element numbering that Ariel and Ahmet cannot figure out how to solve. Will need to get back to this at some point.

Ligaments and Tendons:
Tension test by pulling the bones away from each other. Include one ligament at a time, To test for simulation convergence, Material properties and mesh convergence (parts of calibration phase)

These tests were run by prescribing the displacement of the femur along the z axis (chosen as the anatomical axis), while fixing all other DOF of the femur. All cylindrical joints were set free.
This table gives a brief summary of the results for the Ligament and Tendon tests. Further analysis may be done using the logfile/plotfile results, all saved in the repository
	Stretch along z-axis	total reaction force at full stretch	Maximum fiber stretch	Notes:
FMB-ACL-TBB (ACL tension)	4mm	414 N	1.25	*
FMB-PCL-TBB (PCL tension)	4mm	65 N	1.18	*
FMB-MCL-TBB	4 mm	348 N	1.35	*
FMB-LCL-FBB	4 mm	53 N	1.2	*
PTB-PTL-TBB	4 mm	819 N	1.18	*
PTB-QAT-QSO**	4 mm	1140 N	1.16	*

* could not get prestrain to converge initially. For these tests the Initiliaze step was ignored, and the prestrain was removed from the material definition. Will need to run more tests to get the prestrain working.
**QSO is the rigid body used for the slider joint attached to the top of the quadriceps tendon

Cartilage and Meniscus:
Compression test by pushing the bones towards each other. To test for simulation convergence, mesh convergence.

FMB-FMC-TBC-TBB
-compression test of only 0.1 mm took two hours to converge (all DOF of femur fixed but prescribed displacement in z axis- which is the femur anatomical axis) had to use sliding-facet-on-facet contacts
-tried prescribing flexion axis to zero but leaving all DOF of femur free, too unstable could not converge
- made a coarser mesh for cartilages, still took almost 2h to converge to 0.2 mm, seems like the FMC is too bumpy because couldn't run VCG in smoothing procedures
-redid the segmentation for FMC- made it very smooth in slicer before exporting to STL. Then did VCG just with smaller value. Tried above compression test again 0.2 mm, converged in 4 mins

FMB-FMC-MNS-TBC-TBB
attempt 1: Tibial and Femoral cartilages were changed to rigid, and the only contacts included were between the meniscus and cartilage. This tests only the meniscus properties and contacts. First MNS-L was tested. This case converged, however the contact between the FMC and MNS-L does not seem to be working. Penalty was increased to 10, didn't help.
attempt 2: try leaving cartilages as deformable bodies, but still no contact between cartilages. Seems there is a problem with the MNS and TBC contacts. Appears to be an initial penetration issue. Changing the contact penalty to 100 did not help, neither did turning off augmented Lagrangian…. MNS segmentation were edited to reduce overlap. This fixed the issues.

FMB-FMC-PTB-PTC
femur fixed, patella displaced 0.5 mm in the -y direction, to compress the PTC and FMC. Converged.

Full Model
Compression
Full model compression 200 N applied to femur, flexion angle fixed. Tibia and fibula fixed.
Converged in 2h23min with sliding facet-on-facet contacts
Converged in 1h08min with sliding elastic contacts

Passive Flexion
Full model 45 degree applied to the flexion axis, all other DOF set free. Converged to 98%, took 20 hours. Also noticed the patella was being 'pushed' away from the femur. Upon further inspection realized that the linear springs used were not tension only springs.
-Springs were changed to discrete elements, where the force-displacement relationship is defined in a load curve. Re-ran the model. It only converged to 25%. ran on debug at the end, not immediately clear what is causing problems.
-Tried turning off augmented lagrangian in contacts, only converged to 15%
-tried turning off symmetric stiffness within the contacts, made no difference, converged to 25% in same time as previous model.

Remaining passive flexion model debugging is summarized in the table below:

Note: All models in the chart below were run without the prestrain step, unless otherwise noted
Date	Model Description	File name + location	convergence	notes
unknown	Full knee- 45 degree flexion	Oks003/model_04/Febio_02/Full_45.feb	25 %	Not clear what is causing issues. Tried to turn off augmented lagrangian in contacts, only converged to 15 %
01/25/19 10:35:36 AM	Full model, 90 degree flexion. All ligament contacts were removed.	Oks003/model_05.Febio/Full_90.feb	12 %	Did not affect the convergence, (25 % for 45 degrees vs 12% for 90 degrees) however the model ran more quickly
02/01/19 08:22:14 AM	Patella extensor mechanism and meniscus were removed, 90 degree felxion.	Oks003/model_05/Febio/Full_90_N0Meniscus_NoPatella.feb	58%.	It looks like the MCL is buckling and causing the model to fail.
02/01/19 08:23:22 AM	Same as above, material properties of the ACL ,PCL,MCL, LCL to k=10, c1=0.01.	Oks003/model_05/Febio/Full_90_N0Meniscus_NoPatella_02.feb	100%	The MCL twists , maybe due to the tie surface being inaccurate?
02/04/19 08:36:52 AM	Same as above, MCL tie surface edited to include only few elements at the very top	Oks003/model_06/Febio/Full_90_N0Meniscus_NoPatella.feb	100% (51 hours.)	MCL is penetrating the FMB
02/06/2019	Same as above, MCL contact included	Oks003/model_06/Febio/Full_90_N0Men_NoPat_MCLcontact.feb	100% (61 hours.)	Model runs, however it is unlikely that the MCL tie is realistic
02/11/19 10:42:30 AM	MNS were added back to the model, MCL- MNS tie was left out.	Oks003/model_06/Febio/Full_90_NoPatella.feb	91 %. ( 87 hours)
02/15/19 08:14:47 AM	Same as above, MNS-MCL tie was included.	Oks003/model_06/Febio/Full_90_NoPatella_MCLtie.feb	91 % . (HPC, 60 hours)
02/22/19 08:45:19 AM	New MCL geometry, and insertions. Meniscus and patella removed	Oks003/model_07/Febio/Full_90_NoMen_NoPat.feb	100 % on windows (28 hours) / (seg faulted at 89 % on linux)	Looks good, next will add the meniscus back in and run again
02/28/19 09:07:44 AM	Same as above, meniscus added. No mcl-mns tie	Oks003/model_07/Febio/Full_90_NoPat.feb	76 %, windows (86 hours)	Next will add prestrian.
03/13/19 01:40:04 PM	No patella, no mcl-mns tie. Opt iter changed to 50, max retries 5, aggressiveness 1	Oks003/model_07/Febio/Full_90_NoPat_NewControls.feb	100 % (6 hours, ahmets laptop 4 cpu)	Significant convergence time improvement from changing opt iter
03/14/19 01:39:46 PM	Same as above, Mcl-mns tie added. Tie penalty 1, laugon 0. All material properties were returned to their original intended values.	Oks003/model_07/Febio/Full_90_NoPat_NewControls_MCLTie.feb	100 % (6 hours, ahmets laptop 4 cpu)

Prestrain
Control parameters were copied from example in prestrain plugin downloads package, as well as prestrain constraint parameters.
ALL degrees of freedom of tibia and femur were fixed. Prestrain step would not converge otherwise.
In many cases the stretch along z of the ligament needed to be reduced from 4 mm in order for the problem to even converge to the first step.
For example, when the stretch was set to 4 mm the first step would not converge, but when set to 3 mm the entire problem converged (not sure why this is happening?)

Noticed some issues with the load curve definition. Seems that the load curve for prestrain step needs to run from time 0-1 and then for the loading step from time 1 onwards. Otherwise the prestrain is applied at the same time as the loading step. This was the cause of many of the issues we encountered above.

Tried running a simple test problem with pre-strain to reproduce the result in the prestrain example on the open knee site. Couldn't get comparable results. Emailed Steve to try and get answers, he hasn't responded yet.

Ariel 01/15/19 01:45:39 PM Steve answered some questions for us. The bulk modulus and the fiber element must be defined under the main material element, not the elastic element in a prestrain material. This solved the problem we were having with the test case, and now can reproduce the results from open knee site. Now that this is solved we can revisit prestrain tests with each material.

Ariel 02/12/19 11:37:05 AM ACL, PCL prestrain running fine. Prestrain + 3mm displacement along z converged for both.

Ariel 02/12/19 11:37:05 AM MCL, LCL prestrain causing issues. Test cases were run on “sample” rectangular geometries, and there were no issues with the prestrain settings for MCL, LCL.

Ahmet suggested trying to tie the insertion origins as opposed to setting them as rigid nodes. Still could not converge.

MCL prestrain +3 mm displacement in z direction ran when the prestrain value was reduced to 1.01 (from 1.034). For now we can use that value, and revisit the problem in the calibration phase?

Tried prestrain of 1.01 plus tying the insertion sites, and it did not converge.
LCL also converged only when prestrain was reduced to 1.01 (from 1.027)

Tried changing the update rule from “prestrain” to “in-situ stretch”. Didn't make a difference

Ariel 02/28/19 11:44:55 AM Noticed that the contact surfaces were causing problems in prestrain convegence, so they were moved to the loading step only (this has already been noted in the protocol deviations)

Ariel 03/12/19 03:49:45 PM By changing material properties, we were able to get prestrain + tension test running for ACL, PCL, LCL, MCL individually.
- when trying to run them all at the same time however, any models containing both MCL,LCL failed to converge. found two solutions to this: 1. Run two prestrain steps- by defining new load curves and just copying the initialize step again. 2. Define the prestrain value using the load curve (0,1) (1,1.034), and applying in situ stretch of 1.0 in the material definition. This allows for proper scaling of the in situ stretch . Results differed using the two methods. May need to look into that.
-Once the prestrain was scaling properly, the materials were able to be returned to the initial desired properties. Needed to adjust the control settings for the prestrain step a little bit to allow for smaller step sizes (changes noted in protocol deviations documents)

Ariel 03/14/19 01:44:46 PM Trying to get prestrain + use constraints to move the femur, having some issues.
1. use the constraints to rotate/translate the body without a prestrain step -works
2. When I Include the prestrain step (prestrains all set to 1.0), translate works but rotate doesn't
3. This is also the case even if I don't set any of the material definitions as prestrain materials, so it has nothing to do with the prestrain itself, but something happens after the prestrain step that only affects the rotation of the rigid joints?
Tried playing with moment pentaly, tolerance, angtol, increasing the number of retries, nothing seemed to help.

Natural Knee DU02

Simulation Convergence:

Note: All models in the chart below were run without the prestrain step, unless otherwise noted
Date	Model Description	File name + location	convergence	notes
01/07/19 09:44:35 AM	Full knee 90 degree flexion	DU02/model_01/Febio/Full_90.feb	32%. / ( 74 hours)
01/07/19 09:47:05 AM	Same as above, all ligament contacts removed (besides ACL/PCL)	DU02/model_01/Febio/Full_90_NoLigamentContacts.feb	32%. (21 hours)	Run time improved significantly, likely not all ligament contacts are necessary. Will add them in as needed
01/08/19 08:19:57 AM	Same as above, meniscus were removed.	DU02/model_01/Febio/Full_90_NoMeniscus.feb	60%. ( 79 hours)	The patella is being forced away from the femur- maybe due to patella ligmament being too thick?
01/10/19 01:56:00 PM	90 degree flexion, no ligament contacts, patella extensor mechanism removed	DU02/model_01/Febio/Full_90_NoPatella.feb	60% (97 hours)	Same convergence as no menisucs indicates that something else is causing a problem? Or coincidence?
01/14/19 12:07:32 PM	Same as above, both meniscus and patella removed	DU02/model_01/Febio/Full_90_NoMeniscus_NoPatella.feb	*Seg fault on linux. Ben was able to run on windows / 76.1%	Based on oks003 experience, the issue is likely the MCL.
01/24/19 12:42:01 PM	Full knee 90 degree flexion, QAT, PTL were re-created manually. Ligament contacts removed. QAT joint rotation set free	DU02/model_02/Febio/Full_90_NoLigamentContacts.feb	55 % (69 hours)	Patella still lifting away
02/22/19 08:48:58 AM	90 degree flexion, patella extensor mechanism and meniscus removed. MCL, LCL bulk modulus reduced	DU02/model_02/Febio/Full_90_NoMeniscus_NoPatella.feb	*Seg fault on linux. Ran on windows. 82 % (55 hours)	MCL is twisting. We need to re-do the MCL tie based on what we learned from dissection.
02/26/19 04:02:19 PM	90 degree flexion, patella extensor mechanism and meniscus removed. MCL lofted and ties re-done	DU02/model_03/Febio/Full_90_NoMen_NoPat.feb	Runs on linux. 93.9% (104 hours)	(note for next time: mcl-tbb contact was left off unintentionally- add it back.)
03/07/19 08:25:51 AM	Same as above, Meniscus added	DU02/model_03/Febio/Full_90_NoPat.feb	54.8% (56 hours on Windows)	Maybe a penetration issue with the lofted MCL and the bones?
03/07/19 08:25:51 AM	MCL loft was cut with the bones, above model was repeated.	DU02/model_03/Febio_02/Full_90_NoPat.feb	54.8% (66 hours on Windows)	Same results as above, so issue was not penetration.
03/19/19 09:00:33 AM	Same as above, / control settings updated for speed. All material properties restored to initial intended values. Max aug 1 in all contacts	DU02/model_03/Febio_02/Full_90_NewControls_NoPat.feb	100 % (2 hours!)	The change in max aug made a big difference in convergence speed, but may be specific to this model.
03/20/19 03:05:09 PM	Full knee model, all parts included. Spring added at top of QAT to help hold patella. Stiffness of 10 N/mm.	DU02/model_03/Febio_02/Full_90_NewControls.feb		Adding the spring fixed the problem of the patella lifting off. May need to adjust spring stiffness. QAT to FMB, FMC contacts will need to be added back into the model. The patella is twisting, and pushing the femur forward on the lateral side
03/28/19 08:22:54 AM	Full knee model, QSO slider removed, but spring included 1 N/mm. MPFL, LPFL springs removed	DU02/model_03/Febio_03/Full_90_nosprings.feb

Prestrain:
Ariel 01/17/19 12:10:17 PM Got pre-strain working. Now running prestrain test on each ligament individually to ensure there are not issues/ to check material behavior:

* aiming for approx 10% strains on each ligament
Ligament Name	Approx initial length	Stretch in z direction	Femur reaction at full stretch	Max stress in ligament	Notes
ACL	38 mm	4 mm	255 N	86.1 Mpa
PCL	33 mm	3 mm	327 N	36.3 Mpa
LCL	60 mm	6 mm	61.9 N	73.2 Mpa	*
MCL	62 mm	6 mm	414 N	65.3 Mpa	*
QAT
PTL

*K, c1 needed to be changed for prestrain to converge. K=100, c1=4.36 were the values used in prestrain test problem, and they work, but trying to find k to use that will converge with c1=1.44?

Ariel 01/21/19 08:26:02 AM A simplified rectangular geometry was created to represent the MCL, prestrain was tested using the MCL material properties to check if the problem was geometry-related. Tried various mesh densities. All test cases converged with the original intended MCL material properties.

MCL prestrain converged using knee geometry when prestrain was set to 1.02 (changed from 1.034)
LCL prestrain converged when prestrain was set to 1.015 (changed from 1.027)
Changing the update rule did not have an effect. Still needed to reduce prestrain to above values for convergence