Modeling and Simulation Workflow using Open Knee(s) data
Cleveland Clinic Team
Ariel Schwartz, Snehal Chokhandre, Ahmet Erdemir
06/27/18
Corresponding author: Ahmet Erdemir, erdemira@ccf.org:
# Introduction
## Data Utilized
1. General Purpose MRI (3D T1-weighted without fat suppression, isotropic, 0.5 mm resolution)
2. Cartilage MRI (3D T1-weighted with fat suppression, 0.35 mm sagittal plane resolution, 0.7 mm out of plane resolution)
3. Connective tissue MRI  (proton density, turbo spin echo in sagittal, axial, and coronal planes, 0.35 mm in plane and 2.8 mm out of plane resolution)
## Overview of Target M&S Processes and Outputs
The study aims at developing a three dimensional finite element model of the knee joint and simulate passive flexion while providing detailed specifications for all the intermediate steps taken to accomplish the goal (segmentation, geometries, meshes, assembled model with materials and boundary conditions. And simulation case)
## Detailed M&S Outputs
The Workflow section below provides detailed instructions on how to obtain the following outputs:
Output	Description	File Format
Segmentation	Volumetric reconstruction of tissues of interest, specifically the definition of the boundaries of the tissue, as an image volume	NiFTI (.nii)
Raw Geometry	Geometric reconstruction of the tissues of interest as a surface representation. created from the Segmentation volume, without any smoothing procedures.	stl
Smooth Geometry	Geometric reconstruction of tissues of interest as a watertight surface representation, after applying volume-preserving smoothing procedures.	stl
FEBio Input File	Text file including mesh definition, constitutive models, in-situ strain, Joint definitions, Loading and boundary conditions, and numerical analysis settings	xml

# Workflow
## Image Segmentation
### Target Outcome
Volumetric reconstruction of a tissue of interest, specifically the definition of the boundaries of the tissue, as an image volume, and as a surface representation (STL).
### Burden
Software requirements:
3D Slicer is a free, open source software package for visualization and image analysis (BSD-style open source license, see http://www.slicer.org). Use the latest version of Slicer (4.8) for access to more tools and features. 1

Hardware requirements:
Anticipated Man Hours and Expertise Level:
Computational Cost:
### Protocols
#### Input
Set(s) of MRI in NifTI format (https://nifti.nimh.nih.gov/)
#### Segmentation Procedures
##### Segmentation Algorithms
Several 3DSlicer algorithms that will be used during the segmentation process are described below.
Grow-Cut Segmentation
“Grow Cut Segmentation is a competitive region growing algorithm using cellular automata. The algorithm works by using a set of user input scribbles for foreground and background. For N-class segmentation, the algorithm requires a set of scribbles corresponding the N classes and a scribble for a don't care class.”2
Label Map Smoothing
“This filter smooths a binary label map. With a label map as input, this filter runs an anti-aliasing algorithm followed by a Gaussian smoothing algorithm. The output is a smoothed label map.”2
In the smoothing parameters outlined below, Sigma (Gaussian smoothing parameter) is chosen based on image resolution (e.g. for cartilage MRI with resolution = 0.35 x 0.35 x 0.7 mm, sigma=0.7)
Joint Smoothing
“This will ensure that all resulting models fit together smoothly, like jigsaw puzzle pieces. Otherwise the models will be smoothed independently and may overlap.”2
##### Tissue-Specific Segmentation Procedures
Below are the guidelines for segmentation procedures based on tissue type. It is important to use the specified input MRI, and locate the boundary as described for each tissue. However, the segmentation procedures described are only a suggestion, and one may choose to highlight the anatomy using whichever tools they find most efficient.
Once all tissues have been segmented, the label maps should be saved as NiFTI (.nii) and converted to raw STL from Slicer (without any further smoothing procedures).
Tissue	Input MRI	Boundary Definition**	Grow-Cut Segmentation	Manual Segmentation	Labelmap Smoothing	Joint Smoothing
Registration Markers	General purpose MRI	Will appear bright in the MRI- the outer edge of the bright region defines the boundary	yes*	yes / (fill in screw holes/ bubbles)
Bones (Femur, Tibia, Fibula, Patella)	Cartilage MRI	Cortical bone will appear black in MRI- outer edge of black region defines the bone surface	yes		yes* / sigma=0.7
Cartilage (femoral, medial tibial, lateral tibial, patellar)	Cartilage MRI	Use bone boundary to help define cartilage boundary	yes		yes / sigma=0.7	yes / (with bones)
Menisci / (medial, lateral)	Cartilage MRI	Use cartilage boundary to help define meniscus boundary		yes	yes / sigma=0.7	yes / (with cartilage)
Ligaments and Tendons / (ACL, PCL, Patellar Ligament, Quadriceps Tendon)	Ligament MRI (for boundary definition) / Cartilage MRI (for resolution)	Use bone boundary to help define connective tissue boundary	yes / PHASE 1: / using sagittal ligament MRI	yes / PHASE 2: / using general purpose MRI, overlay labelmap from phase 1 (as foreground layer) and trace boundary ***		yes / (With bones)
Ligaments / (LCL, MCL)	General Purpose MRI	Use bone boundary to help define connective tissue boundary		yes	yes / sigma=0.5

*Always check the slices manually after using Grow-Cut or Labelmap smoothing, and perform touch ups as needed to better define the boundaries.
**Refer to sample images below to help define boundaries
***Alternatively, one can display the ligament specific MRIs and the cartilage specific MRI in different windows. When linked, Slicer uses interpolation for coupled viewing of the image sets that are already spatially aligned. In return, one can do the segmentation on interpolated ligament MRIs using the cartilage MRI as the master volume for segmentation. This allows high resolution segmentation volume from images with lower resolution directly.
##### Sample Images
These images are provided in order to assist with boundary definitions
Bones:

Cartilage:

Menisci:

Connective Tissue - Ligaments & Tendons:
Ligament MRI:

General Purpose MRI:

## Geometry Generation
### Target Outcome
Geometric reconstruction of a tissue of interest as a watertight surface representation, ready for meshing.
### Burden
Software requirements:
MeshLab an open source, portable, and extensible system for the processing and editing of unstructured 3D triangular meshes (GPL license, see http://meshlab.sourceforge.net/).3
Hardware requirements:
Anticipated Man Hours and Expertise Level:
Computational Cost:
### Protocols
#### Input
Surface representation of tissue of interest in STL format in MRI coordinate system (raw, without filtering and smoothing)
#### Smoothing Procedures
A 5 step smoothing procedure (LVTIT) is used on the STLs. This process was found to create uniform meshes, which visually maintaining the geometrical shape of the tissues.
##### Smoothing Algorithms
This section provides brief descriptions of the Meshlab Algorithms used in the process.
Laplacian Smoothing [L]
For each vertex in the mesh, a new position is chosen based on average position with nearest vertex.3
The “Smoothing steps” parameter is the number of times the process is repeated.
Surface Reconstruction: VCG [V]
“Surface reconstruction algorithm that have been used for a long time inside the ISTI-Visual Computer Lab. It is mostly a variant of the Curless at al. e.g. a volumetric approach with some original weighting schemes, a different expansion rule, and another approach to hole filling through solume dilation/relaxations” 3
'Voxel Side' values are chosen relative to original image resolution; e.g. for cartilage images with a resolution of 0.35 x 0.35 x 0.7 mm, use a world unit of 0.35, 0.5, 0.7mm.
Taubin Smoothing [T]
“A lambda- miu smoothing, it makes two steps of smoothing for each iteration. Based on Gabriel Taubin, 'A signal processing approach to fair surface design' Siggraph 1995” 3
Iso Parameterization [I]
Stage 1: Iso Parameterization
“The Filter builds the abstract Isoparameterization of a two-manifold triangular mesh. An adaptively chosen abstract domain of the parameterization is built. For more details see Pietroni, Tarini, and Cignoni, 'Almost isometric mesh parameterization through abstract domains' IEEE Transaction of Visualization and Computer Graphics 2010 “ 3
Stage 2: Iso Parameterization Remeshing
“Remeshing based on Abstract Isoparameterization, each triangle of the domain is recursively subdivided. For more details see Pietroni, Tarini, and Cignoni, 'Almost isometric mesh parameterization through abstract domains' IEEE Transaction of Visualization and Computer Graphics 2010” 3
Sampling Rate determines the number of subdivisions, a.k.a. density of the surface mesh.
##### Specimen Specific Smoothing Parameters:
The table below specifies the parameters to be used in the smoothing processes for each tissue. These values are considered a starting point, and quality assurance should be performed to ensure that there was not significant loss of features or volumes. The process should be performed in the order provided. An X indicates that the smoothing step should be skipped for that tissue.
	1. Laplacian Smoothing / (Smoothing Steps)	2. VCG Surface Reconstruction / (Voxel Side)	3. Taubin Smoothing / (Lambda, mu)	4. Iso Paramaterization / (Sampling Rate)	5. Taubin Smoothing / (Lambda, mu)
Registration Markers	X	X	X	X	X
Femur, Tibia	20	0.7	0.5,-0.53	10	0.5,-0.53
Patella	20	0.5	0.5,-0.53	7	0.5,-0.53
Fibula	20	0.5	0.5,-0.53	5	0.5,-0.53
femoral cartilage	20	0.35	0.5,-0.53	[10,15,20]*	0.5,-0.53
tibial cartilage	20	0.35	0.5,-0.53	[7,10,13]	0.5,-0.53
Patellar Cartilage	20	0.35	0.5,-0.53	[(6),8,10,(12)]	0.5,-0.53
Menisci	20	X	X	[6,8,10]	0.5,-0.53
ACL,PCL	20	0.35	0.5,-0.53	[3,4,5]	0.5,-0.53
Patellar Ligament	20	0.35	0.5,-0.53	[6,8,10]	0.5,-0.53
Quadriceps Tendon	20	0.35	0.5,-0.53	[4,6,8]	0.5,-0.53
MCL	20	0.35	X	[6,7,8]	0.5,-0.53
LCL	20	X	X	[3,4,5]	0.5,-0.53

* Three mesh densities are provided as a guide- the user will determine which mesh density to use in the model based on the following criteria:
Choose the coarsest mesh that
1. Maintains the geometry of the tissue, without visibly losing any features
2. Fits at least 3 triangular elements across the cross section of the thinnest part of the tissue
#### Checking and Repairing the STL
Check that the STL is manifold and watertight. Re-Orient faces coherently so surface normals all point outward.
## Template Model Generation
### Target Outcome
Assembled template model of the knee in Finite Element Analysis software including:
- node, element definitions
- node set, element set, and surface set definitions
- constraint definitions (tie, contact)
### Burden
Software requirements:
SALOME is an open-source software that provides a generic platform for pre- (cad, meshing) and post-processing for numerical simulation (LGPL license, see http://www.salome-platform.org/).
FEBio is a nonlinear implicit FE framework designed specifically for analysis in biomechanics and biophysics (Custom open source license; free for research use, licensing for commercial use is available, see http://www.febio.org) 4

Hardware requirements:

Anticipated Man Hours and Expertise Level:
Note: The process is completed using python scripts. The user is only required to provide the tissue STLs, and the types of constraints between the tissues (in an xml file).

Computational Cost:
### Protocols
#### Input
Explicit surface representation of tissues of interest; in STL format in MRI coordinate system (processed with volume preserving smoothing)
#### Tetrahedral Mesh Generation
Create a mesh from each STL file, using Salome's NETGEN 3D mesh generator.

Settings used for generating the mesh:
Name	Definition	Value
Max Size	maximum linear dimensions for mesh cells.	Equal to the maximum linear dimension of the input STL
Min Size	minimum linear dimensions for mesh cells.	Equal to the minimum linear dimension of the input STL
Fineness	Ranging from Very Coarse to Very Fine allows to set the level of meshing detalization.	Level 4. (If this fails, use Level 3)
Optimize	the algorithm will modify initially created mesh in order to improve quality of elements. Optimization process is rather time consuming comparing to creation of initial mesh.	On

Source of Definitions: http://docs.salome-platform.org/latest/gui/NETGENPLUGIN/netgen_2d_3d_hypo_page.html
#### Creating Surfaces
After creating the meshes, the Tie and Contact surfaces are defined by geometric principles relating a pair of meshes. This step is performed using Salome's python interface:
- Proximity – find all the nodes on part1 that are within a distance X ( related to the element size) of any node on part2.
- Normals – select faces on part 1 that have normal vectors that point toward the barycenter of part 2. This can also be limited by the proximity condition if desired.
- Contains – one mesh contains the other, select elements that have normal vectors that point inward or outward.
- All – all the surfaces.

##### Tie and Contact surface definitions
The following table specifies all the tie and contacts surfaces between tissues, and which geometrical principles should be used to relate them.
Tissue Abbreviations:
FM:femur , TB:Tibia, FB:Fibula, PT:Patella, FC:Femoral cartilage, TLC: Tibial Laterla cartilage, TMC: Tibial Medial Cartilage, PC:Patellar Cartilage, LM:Laterla Meniscus, MM:Medical Meniscus, ACL:Anterior cruciate Ligament, PCL: Posterior cruciate ligament, MCL:Medical Collateral Ligament, LCL: Lateral Collateral Ligament, PL: Patellar ligament, QT: Quadriceps Tendon
Constraint Abbreviations:
C: Contact, T:Tie
p: Proximity, n:Normals, c:contains, a:all

	FM	TB	FB	PT	FC	TLC	TMC	PC	MM	LM	ACL	PCL	MCL	LCL	PL	QT
FM					T:p						T:p	T:p	C:a / T:p	C:n / T:p		C:n
TB						T:p	T:p		T:p	T:p	T:p	T:p	C:a / T:p		T:p
FB														T:p
PT								T:p							T:p	T:p
FC	T:p					C:n	C:n	C:n	C:n	C:n						C:n
TLC		T:p			C:a					C:n
TMC		T:p			C:a				C:n
PC				T:p	C:n
MM		T:p			C:n		C:p						T:p
LM		T:p			C:n	C:n
ACL	T:p	T:p										C:p
PCL	T:p	T:p									C:p
MCL	C:a / T:p	C:a / T:p							T:p
LCL	C:n / T:p		T:p
PL	T:p			T:p
QT	C:n			T:p	C:n

#### Writing the FEBio input file
The following information is written in the FEBio input file (xml) to create the template model:
Materials - at this stage only rigid (bones) or elastic
Nodes- list the node coordinates for each tissue
Elements- list the node connections to define the elements for each tissue
Surface- specify all the elements from a tissue that belong to each defined surface (to be used in tie and contact pairs)
Surface pairs – create connections between the defined surfaces, specify a “master” surface, and “slave” surface.  The following criteria are used:
- The larger of the two surfaces should act as the master surfaces.
- If the surfaces are of comparable size, the surface on the stiffer body should act as the master surface.
- If the surfaces are of comparable size and stiffness, the surface with the coarser mesh should act	as the master surface.
Boundaries- attach deformable bodies to rigid bodies, at this stage set all the rigid bodies to be fixed in place
Contacts – for Tie contacts, define “tied” type between surface pairs. For sliding contacts, define “facet-to-facet sliding” between surface pairs.
Load Data- define the load curves that will be used- “linear”, and “steps”
Outputs- “contact gap”, “contact pressure”, “contact traction”, “displacement”, “reaction forces”, “stress”
Control- define the control parameters for the step. Use FEBio defaults5
Tie
## Material Definitions
### Target Outcome
FEBio input file including material definitions for all tissues in the knee
### Burden
Software requirements:
FEBio is a nonlinear implicit FE framework designed specifically for analysis in biomechanics and biophysics (Custom open source license; free for research use, licensing for commercial use is available, see http://www.febio.org)4

Hardware requirements:

Anticipated Man Hours and Expertise Level:

Computational Cost:
### Protocols
#### Input
FEBio template model input file (.xml)
#### Constitutive Models
##### Bone
Bones are assumed to be rigid bodies, as they have a much higher stiffness than the other knee tissues. This greatly saves on computational cost, and allows for definition of motion through rigid body kinematics.
Bone Properties:
Density: 1.2237e-9 tonnes/mm3 6
This value was taken based on data for cortical bone of healthy female subjects aged 20-29 years (Open Knee(s) specimen is female aged 25 years)
##### Cartilage
Cartilage is modeled as nearly in-compressible Neo-Hookean material. In order to avoid element locking in FEBio, it is recommended to do this by modeling a Mooney-Rivlin material with C2 set to zero. 5
Cartilage Properties : 7
Density [tonnes/mm3]	C1	C2	K
1.5e-9	0.856	0	8

K set to correspond to approximately 0.46 Poisson ratio.
##### Ligaments and Tendons
Ligaments are modeled in FEBio using a nearly incompressible, transversely isotopic, hyperelastic material with a Mooney-Rivlin ground substance.
Ligament Properties: 7
Units are in MPa where applicable
Ligament	Density / [tonnes/mm^3]	C1	C2	K	C3	C4	C5	λm	Source
ACL	1.5e-9	1.95	0	73.2	0.0193	116.22	535.039	1.046	8
PCL	1.5e-9	3.25	0	122	0.1196	87.187	431.063	1.035	8
MCL,LCL	1.5e-9	1.44	0	397	0.57	48	467.1	1.066	9
PTL	1.5e-9	2.75	0	103.3	0.065	115.89	777.56	1.042	8
QAT	1.5e-9

Fiber Direction:
In FEBio, under the material definition, fiber type can be specified as “vector” so that all fibers in the material point in the direction of the vector. 5
The vector direction will be defined as the direction of the longest edge of the oriented bounding box for each ligament.

Material Properties For QAT: Orozco et al 2018 (https://www.nature.com/articles/s41598-018-20739-w) studied different material models for ligaments and tendons. They use a fibril-reinforced porohyperelastic material as one example with the following parameters:
matrix: modulus E = 10 Mpa, poisson ratio v = 0.4 (from here we can obtain C1, C2)
fiber modulus E = 150 Mpa
exponential term for strain dependent permeability M= 7.98
density ratio between primary and secondary fibrils C = 2
initial permeability k0 = 2.9e-15 m^4/Ns
can we relate this to any FEBio material models?

##### Meniscus
Menisci are modeled in FEBio using a nearly incompressible, transversely isotopic, hyperelastic material with a Mooney-Rivlin ground substance.
Meniscus Properties:

	Density / [tonnes/mm^3]	C1	C2	K	C3	C4	C5	λm	Source
Meniscus	1.5e-9	4.61	0	92.2	0.1197	150	400	1.019	10

Alternatively, 11 Gives the following properties for a transversely isotropic model: (Still missing shear modulus, and would need to convert to FEBio coefficients)
E = 20 MPa in radial, axial directions
E = 140 Mpa in circumfriencial directions
poisson ratio = 0.2 in plane of isotropy
poisson ration = 0.3 out of plane

Fiber Direction:
In FEBio, fiber direction can be specified for each element individually, in the ElementData section. 5
The meniscus fibers will be oriented in the circumferential direction.
To do this, a best-fit circle will be approximated to represent the shape of the meniscus from a proximal view. The fibers in each element will be oriented so that they are tangent to the circle at that location.
#### Stabilizing Components
The following components are not tissues of interest, however they are required to stabilize the model. Mechanical springs and joints are used to represent these anatomical structures.
##### Quadriceps Tendon Attachment
The Quadriceps tendons are attached via quadriceps muscles to the proximal end of the femur. Since the quadriceps muscles are not being modeled, this attachment will be simulated using a slider joint.
In order to define a slider joint (rigid cylindrical joint with prescribed rotation set to zero) in FEBio, it must be connected to two rigid bodies.
Two imaginary rigid bodies will be defined for this purpose. The center of mass of both rigid bodies will be at the approximate center of the cross section of the quadriceps tendon at the most proximal end of the tendon.
One rigid body will be fixed to the proximal end of the quadriceps tendon, and the other fixed to the femur.
The axis of the slider joint will be defined as passing through the rigid bodies center of mass, and parallel to the anatomical axis of the femur.
##### Patellofemoral Ligaments
The medial and lateral patellofemoral ligaments (MPFL, LPFL) will be modeled using linear springs.
The insertion points of the patellofemoral ligaments will be located as follows:
MPFL femoral insertion: 0.5*CD from the distal side of the medial condyle, and 0.4*CD from the posterior side or the medial condyle, where CD = anterior-posterior size of the medial condyle, 14
MPFL patellar insertion: superomedial aspect of patella (~ top 1/3) 15
LPFL femoral insertion: 10.6 mm anterior, and 2.6 mm distal to the lateral epicondyle, average width 11.7 mm 16

LPFL patellar insertion: 8mm from superior pole to upper insertion, insertion width ~ 45% of articular surface

*note: epicondyles can be located in the MRI if they are difficult to find on the meshes.

2 springs will be used for each patellofemoral ligament. They will be placed such that the insertion points of the springs span the widths of the insertions described above.

Total spring stiffness for MPFL = 100 N/mm17
Total spring stiffness for LPFL = 16 N/mm 18 (note average age in this study is 72)
## In Situ Strain
### Target Outcome
FEBio input file including in-situ strain applied to the ligaments and tendons.
### Burden
Software requirements:
FEBio is a nonlinear implicit FE framework designed specifically for analysis in biomechanics and biophysics (Custom open source license; free for research use, licensing for commercial use is available, see http://www.febio.org)4

FEBio Prestrain Plugin This plugin implements a general framework for representing pre-strain in a finite element model using a method termed the pre-strain gradient approach. https://febio.org/plugins/ 12

Hardware requirements:

Anticipated Man Hours and Expertise Level:

Computational Cost:
### Protocols
#### Input
FEBio input file (.xml)
#### Pre-Strain Model
In order to apply in-situ strains, the FEBio Prestrain Plugin will be used.
“The gradient of the local mapping from the stress-free to the prestressed reference configuration is represented by F p, which will be referred to as the prestrain gradient. The total elastic deformation gradient F e is determined by the composited deformation gradient, F_{e} = F F_{p} “12
Prestrain porperties:
Prestrain type will be defined as “in-situ stretch”, where the prestrain gradient is calculated based on the initial fiber stretch. The in-situ stretch can be defined at the element level in the ElementData section of the FEBio input file, or the initial stetch can be defined for all fibers in one ligament.
We will use the isochoric prestrain generator option, as the material is assumed to be incompressible.
The update rule type will be chosen as “prestrain”, meaning that Fp will be updated from the initial prestrain gradient given, to eliminate distortion due to incompatibility with the reference geometry (as opposed to enforcing the given in-situ stretch, resulting in possible distortion of the geometry).
We will apply the pre-strain using an elimination of distortion approach, where the goal is to eliminate distortion induced by the incompatibility of the initial pre-strain gradient12 .

In-Situ Stretch:
Literature values for initial stretch in full extention13
(1.0 indicates strain free initial state)
MCL:
Location	Inferior	middle	superior
Anterior	1.015	1.026	1.024
Middle	1.02	1.039	1.052
Posterior	1.027	1.048	1.058

ACL:
Location	Inferior	Middle	Superior
Anterior	1.014	1.020	1.004
Posterior	1.027	1.024	1.004

LCL:
Location	Initial Stretch
Anterior	1.0
Middle	1.0
Posterior	1.08

PCL, PTL, QAT- initial strain set to zero due to lack of experimental data
Since the pre-strain update rule is chosen to eliminate distortion, the above values would only be used as an initial guess for fiber stretch. Due to changes in cross sectional area of the ligament, in order to maintain equilibrium, the FEA solver will update the fiber stretches as needed. Due to this fact, it may be unnecessary for the modeler to define “anterior”, “posterior” etc regions, as the values are likely to change. Thus, one average value will be given as the initial guess for fiber stretch for all regions in the ligament. After the FEA solver determines the updated initial stretch values, they can be compared to the above literature values, and the average initial guess may be calibrated if necessary.

## Coordinate System/Joint Definitions
### Target Outcome
FEBio input file (.xml) including the joints to allow for knee motion
### Burden
Software requirements:
FEBio is a nonlinear implicit FE framework designed specifically for analysis in biomechanics and biophysics (Custom open source license; free for research use, licensing for commercial use is available, see http://www.febio.org)4

Hardware requirements:

Anticipated Man Hours and Expertise Level:

Computational Cost:
### Protocols
#### Input
FEBio input file (.xml)
#### Locating Joint Axes

##### Tibiofemoral Joint
Grood and Suntay Joint Coordinate System 19 (JCS) is used to define this joint. This method requires a definition of a tibial coordinate system (xT,yT,zT) femoral coordinate system (xF,yF,zF), and a Floating axis (FTF).

The following anatomical landmarks will be located on the meshes of the femur and tibia:

1. medial tibial spine (intercondylar eminence)
2. lateral tibial spine (intercondylar eminence)
3. approximate center of medial tibial plateau
4. approximate center of lateral tibial plateau
5. most distal point on the posterior surface of the femur, midway between the medial and lateral condyles
6. medial femoral condyle (most distal point on posterior surface)
7. lateral femoral condyle (most distal point on posterior surface)

Tibial Coordinate System:

Tibial Mechanical Axis (zT-axis): JCS19 defines this axis as passing through the midpoint between the tibial spines proximally, and and the center of the ankle distally. Due to a lack of MRI data of the ankle, we will assume this axis to pass through the same point proximally (midpoint between spines), and extend parallel to the z-direction of the MRI coordinate system. The z-axis is positive in the proximal direction.

Tibial Anterior direction (yT-axis): The cross product between the zT-axis, and a line connecting the approximate center of each tibial plateau. The y-axis is positive in the anterior direction

Femoral Coordinate System:

Femoral Mechanical Axis (zF-axis): JCS19 defines this axis as passing through the center of the femoral head proximally, and the most distal point on the posterior surface of the femur distally. Due to lack of MRI data of the femoral head, we will assume the axis to pass through the same point distally (distal point on posterior surface), and extend parallel to the z direction of the MRI coordinate system. The zF-axis is positive in the proximal direction

Femoral Anterior Axis (yF-axis): The cross product between the femoral mechanical axis (zF-axis) and a line connecting the femoral condyles. The yF-axis is positive in the anterior direction

Flexion Axis (xF-axis): The cross product between the yF-axis and the zF-axis.

Tibiofemoral Floating Axis:

The Tibiofemoral Floating axis (FTF-Axis): Defined as the cross product between the zT-axis and the xF-axis.

##### Patellofemoral Joint
This joint motion is described in a method similar to JCS19, according to Bull et al. 20. This method requires a definition of a patella coordinate system (xP,yP,zP) , femoral coordinate system (same as that described above for the tibiofemoral joint), and a Floating axis (FPF ).

The following anatomical landmarks will be located on the mesh of the patella:

1. medial patella ridge
2. lateral patella ridge
3. midpoint of patella in coronal view

Patella Coordinate System:

Medial-Lateral axis (xP-axis): The line connecting the medial and lateral ridges of the patella.21

Superior-inferior axis (zP-axis): perpendicular to xP and through the midpoint of the patella in coronal view21

Anterior-Posterior axis (yP-axis): cross product between xP-axis and zP-axis.

Patellofemoral Floating axis :

Patellofemoral Floating axis ( FPF-axis): Defined as the cross product between the zP-axis and the xF-axis.

#### Creating the Joints in FEBio

##### Tibiofemoral Joint
In Febio, 3 rigid cylindrical joints5 will be added to the to constraints section to define tibiofemoral motion.

Two “imaginary” rigid bodies must be defined:
Imaginary_Body_1: located at the origin of the tibial (xT,yT,zT) coordinate system.
Imaginary_Body_2: located at the origin of the femoral (xF,yF,zF) coordinate system.

The three rigid cylindrical joints will be defined as follows:
Motion	joint_origin	joint_axis	body_a	body_b
Felxion-extension	Origin of (xF,yF,zF)	xF-axis	Femur	Imaginary_Body_1
External-internal	Origin of (xT,yT,zT)	zT-axis	Imaginary_Body_2	Tibia
Abduction-adduction	Intersection of FTF-axis and xF-axis	FTF-axis	Imaginary_Body_1	Imaginary_Body_2

All other parameters in the rigid cylindrical joints will be set to FEBio defaults 22

##### Patellofemoral Joint
In Febio, 3 rigid cylindrical joints5 will be added to the to constraints section to define patellofemoral motion.

Two more “imaginary” rigid bodies must be defined:
Imaginary_Body_3: located at the origin of the patella (xP,yP,zP) coordinate system.
Imaginary_Body_4: located at the origin of the femoral (xF,yF,zF) coordinate system.

The three rigid cylindrical joints will be defined as follows:
Motion	joint_origin	joint_axis	body_a	body_b
Patellar felxion and shift	Origin of (xF,yF,zF)	xF-axis	Femur	Imaginary_Body_3
Patellar tilt	Origin of (xP,yP,zP)	zP-axis	Imaginary_Body_4	Patella
Patellar rotation	Intersection of FPF-axis and xF-axis	FPF-axis	Imaginary_Body_3	Imaginary_Body_4

All other parameters in the rigid cylindrical joints will be set to FEBio defaults22
## Passive Flexion Simulation
### Target Outcome
Finite Element simulation of Passive Flexion in FEBio
### Burden
Software requirements:
FEBio is a nonlinear implicit FE framework designed specifically for analysis in biomechanics and biophysics (Custom open source license; free for research use, licensing for commercial use is available, see http://www.febio.org)4

Hardware requirements:

Anticipated Man Hours and Expertise Level:

Computational Cost:
### Protocols
#### Input
FEBio input file (.xml)
#### Passive Flexion Definition
We define passive flexion as the relative motion of the femur with respect to the tibia in flexion-extension plane, such that all other rotations are unconstrained, and forces are minimized.
#### Create Motion in FEBio
In order to define the passive flexion motion in FEBio, the tibia will be fixed in place, and then the rotation of the flexion-extension joint will be prescribed to 90 degrees.
All the other tissues and joints will be left unconstrained
#### Run FEBio Simulation
Run the passive flexion simulation case. Hope that (by some miracle) it converges.
# References

1.	Kikinis, R., Pieper, S. D. & Vosburgh, K. G. 3D Slicer: A Platform for Subject-Specific Image Analysis, Visualization, and Clinical Support. in Intraoperative Imaging and Image-Guided Therapy (ed. Jolesz, F. A.) 277–289 (Springer New York, 2014). doi:10.1007/978-1-4614-7657-3_19
2.	Documentation/4.8/Modules - SlicerWiki. Available at: https://www.slicer.org/wiki/Documentation/4.8/Modules. (Accessed: 31st May 2018)
3.	Cignoni, P. et al. MeshLab: an Open-Source Mesh Processing Tool. in Sixth Eurographics Italian Chapter Conference 129–136 (2008).
4.	Maas, S. A., Ellis, B. J., Ateshian, G. A. & Weiss, J. A. FEBio: Finite Elements for Biomechanics. Journal of Biomechanical Engineering 134, 011005 (2012).
5.	Maas, S., Rawlins, D., Weiss, J. & Ateshian, G. FEBio Finite Elements for Biomechanics: Theory Manual. (2010).
6.	Yuen, K. W. K. et al. Characteristics of age-related changes in bone compared between male and female reference Chinese populations in Hong Kong: a pQCT study. Journal of Bone and Mineral Metabolism 28, 672–681 (2010).
7.	Erdemir, A. & Sibole, S. Open Knee: a three-dimensional finite element representation of the knee joint. User’s Guide, Version 1.0.0. (2010).
8.	Peña, E., Calvo, B., Martínez, M. A. & Doblaré, M. A three-dimensional finite element analysis of the combined behavior of ligaments and menisci in the healthy human knee joint. Journal of Biomechanics 39, 1686–1701 (2006).
9.	Gardiner, J. C. & Weiss, J. A. Subject-specific finite element analysis of the human medial collateral ligament during valgus knee loading. Journal of Orthopaedic Research 21, 1098–1106 (2003).
10.	Shriram, D., Praveen Kumar, G., Cui, F., Lee, Y. H. D. & Subburaj, K. Evaluating the effects of material properties of artificial meniscal implant in the human knee joint using finite element analysis. Scientific Reports 7, (2017).
11.	Hull, M. L. A Finite Element Model of the Human Knee Joint for the Study of Tibio-Femoral Contact. Journal of Biomechanical Engineering 124, 273 (2002).
12.	Maas, S. A., Erdemir, A., Halloran, J. P. & Weiss, J. A. A general framework for application of prestrain to computational models of biological materials. Journal of the Mechanical Behavior of Biomedical Materials 61, 499–510 (2016).
13.	Dhaher, Y. Y., Kwon, T.-H. & Barry, M. The effect of connective tissue material uncertainties on knee joint mechanics under isolated loading conditions. Journal of Biomechanics 43, 3118–3125 (2010).
14.	Stephen, J. M., Lumpaopong, P., Deehan, D. J., Kader, D. & Amis, A. A. The Medial Patellofemoral Ligament: Location of Femoral Attachment and Length Change Patterns Resulting From Anatomic and Nonanatomic Attachments. The American Journal of Sports Medicine 40, 1871–1879 (2012).
15.	Aframian, A., Smith, T. O., Tennent, T. D., Cobb, J. P. & Hing, C. B. Origin and insertion of the medial patellofemoral ligament: a systematic review of anatomy. Knee Surgery, Sports Traumatology, Arthroscopy 25, 3755–3772 (2017).
16.	Shah, K. N., DeFroda, S. F., Ware, J. K., Koruprolu, S. C. & Owens, B. D. Lateral Patellofemoral Ligament: An Anatomic Study. Orthopaedic Journal of Sports Medicine 5, 232596711774143 (2017).
17.	Elias, J. J. & Cosgarea, A. J. Technical Errors during Medial Patellofemoral Ligament Reconstruction Could Overload Medial Patellofemoral Cartilage: A Computational Analysis. The American Journal of Sports Medicine 34, 1478–1485 (2006).
18.	Merican, A. M., Sanghavi, S., Iranpour, F. & Amis, A. A. The structural properties of the lateral retinaculum and capsular complex of the knee. Journal of Biomechanics 42, 2323–2329 (2009).
19.	Grood, E. S. & Suntay, W. J. A joint coordinate system for the clinical description of three-dimensional motions: application to the knee. J Biomech Eng 105, 136–144 (1983).
20.	Bull, A., Katchburian, M., Shih, Y.-F. & Amis, A. Standardisation of the description of patellofemoral motion and comparison between different techniques. Knee Surgery, Sports Traumatology, Arthroscopy 10, 184–193 (2002).
21.	Suzuki, T., Hosseini, A., Li, J.-S., Gill, T. J. & Li, G. In vivo patellar tracking and patellofemoral cartilage contacts during dynamic stair ascending. Journal of Biomechanics 45, 2432–2437 (2012).
22.	Help - Eclipse Platform. Available at: http://help.mrl.sci.utah.edu/help/index.jsp. (Accessed: 22nd May 2018)