Summary of oks003 Mesh Properties Confirmation

12/12/19 Based on the results of mesh convergence, converged mesh density models were taken from mesh convergence phase (protocol deviation, it was written that we would make these models from scratch but I realized we already has the identical models from mesh convergence). Once we have the results of this stage, we can go back and retrieve the desired MED files from the mesh convergence folders, and update the model properties file with the desired material properties. Then we can create the full model with calibrated mesh densities and material properties.

12/21/19 wrote a script to read logfile from ligament stretching and fit a line to final 1/3 of the force displacement curve (linear portion) to determine stiffness. StiffnessFromLog.py

looking to get within 2 standard deviations of literature stiffness values

ligaments:

Tissue	Displacement in fiber direction [mm]	Desired Linear Stiffness Range [N/mm]	Initial guess c5	Measured linear stiffness [N/mm]	Final guess c5	Measured Linear stiffness / [N/mm]
ACL_IP8	3	242±28	535	125	5000	195
LCL_IP6	5	59±12	467	25	2000	66
MCL_IP7	5	63±14	467	56	467	56
PCL_IP6*	5#	258±62	431	26	8000	159

 # protocol deviation changed to 5 mm because the last 1/3 of the force displacement data was not all linear with 3 mm
* protocol deviation - ended up having to change fiber directions to be element- wise for pcl instead of all in the long direction of the bounding box. Instead, fiber direction was found by:
- finding the medial plane of nodes in the pcl (using medial_surface.py)
- getting the normals of the nodes in meshlab using “calculate normal for point sets”
- finding the bounding box of the pcl, and getting the vector along the shortest box edge
- for each element in the PCL, find the nearest medial node, and take the cross product between the normal and the shortest edge vector.

Notes on how the pcl issues were resolved:

12/27/19
*PCL6
unexpected results…
c5  = 431.063 , k= 26.812
c5 = 8000, k = 37.57
c5 = 80000, k = 42.28

created a test model of a rectangular sample with pcl properties to test how the material should behave with ideal geometry…
c5 = 431, k=138.15
c5 = 4310, k=522

so it seems to be a geometry issue...

01/07/2020
Will try with a different mesh density for the PCL to see if its an overall geometry shape issue, or if it is specific to that mesh.

PCL8
c5  = 431.063 , k= 28
c5 = 4310, k=38

PCL4
C5 = 431.063, k=29
C5=4310, k=44

Doesn’t seem to make much difference between mesh densities, so it must have to do with the overall shape of the PCL tissue.

Maybe it has to do with the fiber orientation compared with the shape of the pcl (it kind of curves at the fmb)?

2/6/2020 created a PCL6 model with the fiber directions element wise (calculated by taking the medial surface points, getting their normals, each elements closest medial point normal cross with the shortest bounding box edge vector is the fiber direction.
C5 = 431.063, k=44.68
c5 = 4310, k=92.76
c5 = 6000, k=99.58
c5 = 8000, k=105.12

A little better, but still not converging as well as it should
maybe not displacing it enough for the 3rd half to be linear? Try displacing 5 mm instead of 3

c5 = 8000, k=159.14

Tendons:
Tissue	Displacement in fiber direction [mm]	Desired Modulus Range [MPa]	Reference length [mm], cross sectional area [mm^2]	Initial guess c5	Measured linear stiffness [N/mm], / Modulus [MPa]	Final guess c5	Measured linear stiffness [N/mm], / Modulus [MPa]
PTL_IP6	5	337.8.±67.7	L=61.3502 / A=32.2555	777.56	K=420.6347 / E =800.05	337.8	K=252.873 / E=480.96
QAT_IP6	5	255.3±64.1	L=72.9695 / A=66.1315	777.56	K =578.8028 / E =638.651	255.3	K= 318.736 / E= 351.69

* when c5 was set to the average modulus in the range, measured modulus fell within 2 standard deviations, which is a good sanity check.

Cartilage:

1/14/20
this image is from the paper we are using https://www.ncbi.nlm.nih.gov/pubmed/16621620

We are trying to mimic the test done on group3 – lateral tibial plateau covered by the meniscus.

The model was created by:
1. make a template febio model of the TBC-L and TBB using the med files
2. in preview, load the template model. create a 1mm diameter flat ended cylindrical indenter in the general area where we want to test
3. position the indenter perpendicular to the surface at the location of the indentation, using preview translate and rotate features.

Protocol deviation: prescribing a force to the indenter caused instability in the model. Instead, a displacement was prescribed to induce a force of about 0.5 N and the stiffness was measured from the force-displacement results. The indenter was displaced along the axis of the cylinder.

Results:

Tissue	Desired Linear Stiffness Range [N/mm]	Initial guess C1, K	Measured linear stiffness [N/mm]	Final guess C1, K	Measured linear stiffness [N/mm]
TBC-L_IP6	20.38±5.32	C1 = 2.54 / K=100	45.56	C1 = 1.25 / K*=50	23.5

*C1 was adjusted and K was chosen to maintain the same ration C1:K as the initial guess

Note:
I performed the same test on a higher density caritlage mesh out of curiosity, since the indenter was so small compared to the mesh size, I suspected the results may differ. With TBC-L_IP12, using the initial guess for C1, K Stiffness was measured as 33.64 N/mm.

Ariel and Snehal discussed this: Each of the cartilages has its own converged mesh density, meaning that the results of indentation test on each cartilage would yield different results. However, the purpose of this material properties confirmation is more to confirm that we are in the general expected range. Since the test at the higher mesh density yielded less than an order of magnitude difference, we will just assume that all other cartilages would yield similar results. Thus our guess of C1, K are “good enough” for all cartilages.

Meniscus:
c5 will be set to 92 Mpa as it fall within the range of reported values.

9/3/20 After playing around with material properties in du02, we used the following methods for calibration with coupled materials

Keep bulk modulus (k) fixed
Reduce c1 until compressive loads are under 1 N
Calibrate c5 as above to get linear stiffness within expected range.
Check the influence of c1 on tension results – does reducing c1 further have a significant influence on the reaction force? (10%) if yes, continue to reduce c1 until no longer influence. If c1 was adjusted, repeat step 3
Test with in situ strains 0.9,1.1 to make sure we get the expected movement of the curve

Just to have it, will perform the same calibration for oks003 ACL,PCL,LCL,MCL

ACL:
Compression 3 mm – reaction force 35
C1/100 compression 3mm –reaction force 0.649 < 1 N
Tension 3mm reaction 46.4 stiffness 23.23
C5 * 10 Tension 3 mm reaction 105 stiffness 59.35
C5 *10 Tension 3 mm reaction 269 stiffness 201
Check c1/10 error termination