Open Knee(s) preliminary data and tissue quality analysis

Provided by,

Snehal Chokhandre
Ceylan Colak
Specimen	Age	Gender	Side	Protocol deviations	MRI quality **	Cartilage / degeneration *	Joint data quality
oks001	71	Male	Right	Notes	Good	None	No obvious deviations/concerns
oks002	67	Female	Right	Notes	Poor	Severe	No obvious deviations/concerns
oks003	25	Female	Left	Notes	Good	Mild	No obvious deviations/concerns
oks004	46	Female	Right	Notes	Poor	Moderate	Posterior drawer test was not a pure laxity test
oks006	71	Female	Right	Notes	Good	Moderate	No obvious deviations/concerns
oks007	71	Male	Right	Notes	Acceptable	Mild	No obvious deviations/concerns
oks008	40	Male	Right	Notes	Good	None	No obvious deviations /concerns
oks009	34	Male	Left	Notes	Acceptable	Mild	Robot malfunction resulted in large forces and moments applied to the knee which may have resulted in damaged tissue.

Table 1: Assessment of tissue and data quality.

* Based on cartilage grading done by radiologist.

** Good: All tissues of interest are visible and no obvious indication of tissue damage (including bones). All MRI sets aligned. Joint data
     quality is acceptable.
     Acceptable: Most tissues of interest visible and no obvious indication of tissue damage. All MRI sets aligned. Joint data quality is
     acceptable.
     Poor: Tissue quality visibly poor, more than two tissues difficult to demarcate. MRI sets not aligned. Joint data quality is not acceptable.

Tissue quality analysis based on MRI

Magnetic resonance images (MRI) of cadaver knee specimens are based on the osteoarthritis (OAI) MRI protocol of Peterfy Cg et al (1). An assessment of the articular structures of the cadaver knees was made by a trained radiologist using whichever available sequences provided the best information. The methodology used here for scoring the MRI are based on those reported by Meredith et al (2). The scales for evaluating cartilage and bone marrow lesions were based on previous reports (3,4,5).

Cartilage damage score (CDS) developed by Meredith et al (2), was used to capture the total burden of cartilage involvement. It was calculated as the sum of all cartilage damage severity and lesion size scores across all regions of the knee. Categories of none, mild, moderate and severe for cartilage signal and for cartilage lesion size were used. Cartilage was evaluated in 17 different regions (anterior, middle and posterior thirds of medial femoral, lateral femoral, medial tibial and lateral tibial as well as three patellar regions and two trochlear regions).

Cartilage degeneration was categorized none, mild, moderate and severe. The scores for all osteophytes in a compartment were totaled and scored from 0 to 3. Subchondral sclerosis was similarly reported as present or absent for the medial, lateral and patellofemoral knee compartments and then final score determined by number of the 3 knee compartments with evidence of sclerotic change.

Since the MRI were obtained postmortem, synovitis, bone marrow edema and effusion could not be graded exactly. It was a suboptimal evaluation.

Specimen	Cartilage	Osteophytes	Bone marrow lesions	Effusion	Synovitis	Subchondral sclerosis	Meniscus	Ligaments /other soft tissues
oks001	None	None	None	None	None	Absent	None	None
oks002	Severe	mild	mild	None	None	Mild	Tear, degeneration	None
oks003	Mild	None	None	None	None	Absent	None	None
oks004	Moderate	None	Severe	None	None	Moderate	None	None
oks006	Moderate	Mild	None	None	None	Mild	None	None
oks007	Mild	None	None	None	None	Absent	Degeneration	None
oks008	None	None	None	None	None	Absent	None	None
oks009	Mild	None	Mild	None	None	Absent	None	None

Table 2: Detailed tissue quality analysis using all available MRI sets

Important protocol deviations and notes:

oks001

Specimen preparation:

- The order of digitization for tibia markers is a deviation from the specifications. Nonetheless, this order is the same for oks004.
- Femur and tibia was cut 7.5 inches from the epicondylar line (rather than 8 for femur, 7 for tibia). Specifications were updated for all remaining specimens.

Joint imaging:
The posterior region of the knee was dissected further (removal of skin, fat, and muscle layers) to allow fitting of the whole specimen and the patellafemoral registration marker assembly in the transportation fixture (therefore the knee coil of the MRI).
The tibia end of foam to secure the tibia during transportation and imaging had to be cut lower to accommodate fitting of the whole specimen and the patellofemoral registration marker assembly in the transportation fixture (therefore the knee coil of the MRI).

oks002

Specimen preparation:

In specimen dissection, proximal and distal tissue regions (for femur and tibia, respectively) were marked as 4.5 inches. This is needed to accommodate symmetric bone cutting levels. THIS IS A SPECIFICATION UPDATE to accommodate flipping of the joint between tibiofemoral and patellofemoral testing.
Joint imaging

Specimen was inserted tibia first in scanner.
oks003

Specimen preparation:
- Femur registration markers were assembled medially, laterally, and posteriorly (rather than anteriorly or anteromedially). Registration marker probing order was also changed to lateral, medial, posterior. Tibia registration markers were assembled per the specification. Probing order is the same as the specification: lateral medial posterior.
- Ten points (not twelve) were collected on each registration marker. The specifications may need to change as per Robb this has been how the system was set up all the time.
Joint testing

- In tibiofemoral joint testing, passive flexion (for coordinate system optimization) was conducted at 50 N compressive load. Specifications state a 100 N compressive load should be used. All previous specimens has been tested under 50 N compressive load for coordinate system optimization. The relevant protocol may need to be updated this.
- In tibiofemoral joint testing, robotic testing of combined loading at 90 degrees flexion ended prematurely. An additional trial was conducted to complete the tests.
- In patellofemoral joint testing, a coordinate system transformation matrix in SimVitro (the matrix that establishes the relationship between the tibia and load cell) needed to be mirrored to accommodate the left knee.
- In patellofemoral joint testing, at 0 degrees flexion multiple trials were collected for 20, 100, 200, 300, 400, 500 N quadriceps loading. This was necessitated by troubleshooting tendon freeze clamping and tendon actuator response.
oks004

Specimen:

- Specimen Characteristics. Donor age (46 yrs) does not match specifications.
- Specimen Size. The specimen is not hip to toe rather mid-femoral shaft to toe.
Specimen preparation:

Femur Anatomical Landmarks. As the specimen did not include femoral head, landmarks on femoral shaft at its most proximal circumference were digitized.

- Registration Markers – Preparation. Drilling axis (for screw placement) and marker center are not concentric. Careful handling is necessary not to rotate the markers after their installation on bones. Preparation of the markers beforehand, by drilling on the lathe may be helpful to establish concentricity.
- Registration Markers – Digitization. Digitization order for femur spherical markers are: 1 - anteromedial, 2 - medial, 3 - lateral. Digitization order for tibia spherical markers are: 1 - lateral, 2 - medial, 3 – posterior.
Joint imaging preparation:

- Patella registration marker assembly was not placed on the patella for imaging. Alternative imaging or digitization is necessary to align patella local coordinate systems between imaging and motion analysis. This can be accomplished by i) imaging patella only with the registration marker assembly after dissection, or ii) by digitizing patella anatomy using Optotrak along with patella motion analysis markers. Snehal will follow up to resolve this issue.
- As an alternative solution to obtain the transformation matrix between the patella Optotrak marker coordinate system to image coordinate system, 48 points on the anterior bony surface of the patella was digitized using the Optotrak probe. First (and last) three points correspond to lateral, medial, and inferior points, respectively.
- In reviewing the imaging it appears the specimen moved slightly for the general purpose imaging set. No difference in anatomy location was identified between cartilage and other imaging sets. However, the general purpose imaging set was slightly different than the other 4 sets. Caution should be used when segmenting with the general purpose image set.
Imaging:

- After localizer ACRT1 Axial test (a localizer/scout) was ran
- Carl Winalski, MD briefly evaluated the images provided herein; his important comments are provided below:
- The reconstructions on the 3D FLASH sequence shows a banding artifact. This is likely because of the way the images are scaled during the initial image production.
- The FOV looks rather large, raising concern about in-plane resolution, but maybe this is what is needed and the acquisition was adjusted by using a large matrix.
- The specimen has extensive bone infarctions. This is very unusual, but can be seen following high dose steroid treatment such as for bone marrow transplantation. This may not be good for use as a “normal” or simple “degeneration.”
- The high signal in the quadriceps and patellar tendons is from magic angle effect (tendon oriented 55 degrees to main magnetic field). Different positioning may accommodate this issue.

oks006

Specimen preparation:

Femur registration markers were assembled medially, laterally, and posteriorly (rather than anteriorly or anteromedially). Registration markers were digitized in the following order: medial, lateral, posterior. This was done to accommodate the quadriceps tendon.

Joint mechanics:

Fibula was fixed to tibia with a wood screw immediately after imaging before potting. This practice was adapted for oks003 and other previous specimens in various forms. The specifications may need to change to reflect this.

In tibiofemoral joint testing, during combined loading at 30 degrees flexion, the testing ended prematurely with abrupt loading. The test was repeated, in following the scheduled reproducibility testing was conducted and visually compared to first reproducibility testing. Any differences (<0.5 mm translation at peak loads) were attributed to specimen conditioning (and possibly creep).
In patellofemoral joint testing, some conditions needed to be repeated as a result of load application issues and robot shut down. The last trial of these conditions should be used for future data analysis.

oks007

Testing:
- During tibiofemoral joint testing, 1 Nm internal rotation torque (IE laxity testing at 30 & 90 degrees flexion -- possibly others too) was not captured properly. The IE torque was at 0.5 Nm and off-axis loads (varus) were not minimized to zero. Other levels of loads were fine. A separate trajectory was ran with 1 Nm internal rotation torque starting at 90 degrees flexion down to 0 degrees flexion.
- During patellofemoral joint testing at 0 degrees flexion the sensor did not register much pressure and the location of the pressure sensor needed to be readjusted after the test to accommodate higher flexion angles.
- During patellofemoral joint testing during 30 degrees flexion there was a discontinuity in pressure measurements on the medial side. This may be attributed to sensor wrinkling or cartilage degradation at that area (needs to be checked).
- During patellofemoral joint testing at 60 degrees flexion, 600 N loading was repeated as the clamp cover hose was suspected to catch the fixture edge.

oks008
Testing:
- Drill bits to secure the pots were not placed during specimen preparation. This was noticed during the first reproducibility test of the tibiofemoral joint. The specimen was taken down from the robot for placement of drill bits and remounted afterwards. The first reproducibility test (AP laxity at 30 degrees flexion) was repeated after placement of drill bits. The tibiofemoral joint experimentation continued as planned afterwards.
- For tibiofemoral joint testing, at 0 degrees flexion testing conditions, the robot and the control computer lost communications. The system needed to be rebooted. The experiments continued starting with 0 degrees flexion testing.
- For tibiofemoral joint testing, the final reproducibility test illustrated a shift in all translations (as observed from robot measured kinematics).
- Force data was filtered up through 200N 15 degrees PFJ Testing. After this point data was not filtered.
- We will need to check and see if previous PFJ Testing had force torque filtering. All TFJ Testing did not have filtering.

oks009
Specimen:
X-ray evaluation was not possible due to lack of X-ray imaging of the specimen.
Testing:
During tibiofemoral joint testing, the first passive flexion test completed. During extension, the robot malfunction resulted in large forces and moments to be applied on the knee This may have resulted in damage of knee structures. In the second passive flexion test, flexion was completed yet during extension the same malfunction was observed. It may be possible to compare the first passive flexion curve (response of the intact joint) with the second passive flexion curve (response of the potentially damaged joint) to assess any discrepancies due to tissue failure. It may be necessary to consider this specimen as a damaged specimen. The group decided to collect tibiofemoral joint testing data per specifications anyways. The loading and kinematic profiles of the abrupt extension profiles were saved to be able to simulate potentially damage inducing simulation scenarios. If damaged, the laxity and combined loading data may serve modeling & simulation of an injured knee.
- Following robot maintenance, the tibiofemoral joint testing restarted. Passive flexion testing data was qualitatively compared to first passive flexion test (before robot malfunction and large loads being applied to the knee). There was an agreement but this may not warrant lack of any damage to ligaments, menisci, and cartilage.
- During tibiofemoral joint testing, posterior drawer tests (for 30, 60, and 90 degrees flexion) were repeated due to non-zero (unminimized) external rotation moment.
- Specifications of all force transducers, specifically the Theta transducer, should be added to the wiki page on infrastructure for joint mechanics testing.
- Before patellofemoral joint testing, troubleshooting in simVitro (robot control and data collection) needed to be performed. This delayed start of patellofemoral joint testing. Previous scripts to move from tibiofemoral joint testing placement settings to patellofemoral joint testing placement settings did not work due to recent updates to SimVitro. This step was handled manually and the script will need to be updated in future. This does not affect the data.
- During patellofemoral joint testing, for 60 degrees flexion, the tibiofemoral joint equilibrium state to represent passive flexion seemed deviating from its original state. It may be possible that multiple equilibrium states may exist, i.e particularly for internal/external rotation. The equilibrium state was found without any quadriceps load (rather than a minimal ~10 N load) and experiment was conducted. Testing for 45 degrees flexion was also repeated; the pressure sensor location was adjusted before these repeat tests. It should be noted that tibiofemoral joint kinematics and kinetics were collected at all times.
- During patellofemoral joint testing, for 60 degrees flexion and 200 N quadriceps loading, kinematics/kinetics data were collected twice whereas pressure data were collected once. The latter kinematics/kinetics data correspond to the pressure data.

References:

C. G. Peterfy, M.D., Ph.D.†,*, E. Schneider, Ph.D.‡,§, and M. Nevitt, Ph.D.∥ The osteoarthritis initiative: report on the design rationale for the magnetic resonance imaging protocol for the kneeOsteoarthritis Cartilage. 2008 December ; 16(12): 1433–1441.

Meredith, D. S. et al. Empirical evaluation of the inter-relationship of articular elements involved in the pathoanatomy of knee osteoarthritis using magnetic resonance imaging. BMC Musculoskelet. Disord. 10, 133 (2009).

1. Biswal S, Hastie T, Andriacchi TP, Bergman GA, Dillingham MF, Lang P: Risk factors for progressive cartilage loss in the knee: A longitudinal magnetic resonance imaging study in fortythree patients. Arthritis Rheum 2002, 46:2884-92.
2. Yoshioka H, Zou KH, Bhagwat JG, Neumann G, Meredith DS, Lang P: Location-specific intra- and inter-reader reproducibility of MRI cartilage scoring in the knee joint. [Abstract] 18th ECR 2006 [http://www.abstractsonline.com/viewer/?mkey=%7B6748FA35%2DD7A5%2D44B0%2DB8D4%2D4E2E5185 0B06%7D].
3. Neumann G, Mendicuti AD, Zou KH, Minas T, Coblyn J, Winalski CS, Lang P: Prevalence of labral tears and cartilage loss in patients with mechanical symptoms of the hip: evaluation using MR arthrography. Osteoarthritis Cartilage 2007, 15:909-17.