Clarification on Patella Registration Coordinate Systems
Connor Lough

After running the transformation scripts found at <https://simtk.org/websvn/wsvn/openknee/utl/Registration/>, we now have the coordinates of the patella registration marker in Optotrak sensor coordinates as well as in anatomical imaging coordinates. However, we need the final link between the two. We need a transformation between the Optotrak sensor coordinate system and the anatomical imaging coordinate system.

During testing when the patella is registerred, the following process occurs:

1. A wooden block is mounted to the robot. Mount the patella sensor to one of the brass plugs. Mount a reference marker to the other. The reference marker can be any of the other ones.
2. Record the position of the patella sensor relative to the reference marker. This is recorded in the 'Registration marker relative placement.tdms'.
3. Data is collected for about 10 seconds but can be averaged to find the position.
4. Next, the patella marker is removed from the wooden block and the patella MRI marker is mounted.
5. This marker is digitized and the position of the 12 divot points with respect to the reference marker are recorded. The data is saved in a state configuration file under the section "Reference Marker Sensor'.

PAT_OPT
REF_OPT
MRI_SPH

MRI_DIVOTS
REF_OPT

With that being said, we can establish a transformation between the two coordinate systems.

The math behind the transformation is as followed:

Variables:
T[MRI-SPH_PAT-OPT] = Transformation from Patella Optotrak to MRI Spheres
T[MRI-SPH_MRI-DIVOTS]= Transformation from MRI Divots to MRI Spheres, this can be found in the cad dimensions and is already done by PFSphereTransform.py
T[MRI-DIVOTS_REF-OPT]=Transformation from Reference Marker in Optotrak to MRI Divots in Optotrak, can be found in state file (collected points RB2 and position sensor RB2).
T[REF-OPT_PAT-OPT]=Transformation from Patella Optotrak to Reference Optotrak, can be found in tdms file.
T[World_REF-OPT] = Transformation from Reference Optotrak to World, can be found in tdms file.
T[World_PAT-OPT] = Transformation from Patella Optotrak to World, can be found in tdms file.

Transformation:

T[MRI-SPH_PAT-OPT] = T[MRI-SPH_MRI-DIVOTS] x T[MRI-DIVOTS_REF-OPT] x T[REF-OPT_PAT-OPT]

where,

T[REF-OPT_PAT-OPT] = T[World_REF-OPT]^-1 x T[World_PAT-OPT]